## Slide 1: An introduction to Embedded Systems

## Slide 2: About the Trainers
Deepak Nayak
20+ years in Embedded
  R&D
  Projects, Programs, Products
  Delivery
  Startups
Areas
  Consumer AV (DSP, Multimedia)
  Smart Lighting
  HVAC Energy
  Storage
  Data Centre / Cloud
Strong innovation mindset
  Patents, trade secrets
  AI/ML
Rushikesh Kulkarni
3+ years of Training
  Embedded courses
    PG Diploma
3+ years of Industry
  Electronics
    Appliances
    Automotive
Areas:
  Hardware
    Microcontrollers
    Robotics

## Slide 3: OPEN QUESTION!
What does this picture mean?
What is special about what this guy has done?
How is this Embedded Course related to this guy?!

## Slide 4: THE WORLD TODAY
EMBEDDED plays a central role in today’s world
  Professional life
    Desktops, PCs, Notebooks
    Smartphones
  Financial life
    Smartphones
      ATM
      PAYTM/UPI/Online transfer, Online banking
  Personal life
    Smartphones
      Calling, Video-Calling
    Travel
      Ola/Uber, IRCTC/Cleartrip/Makemytrip
    Shopping
      Flipkart, Amazon, Myntra
Now add pandemic and lockdown to the picture!

## Slide 5: AGENDA
5
System
  Embedded System
  Components
  Classifications
Hardware
  Processors
  Other Components
Software
Applications
  Automotive Domain

## Slide 6: SYSTEM
6
What is a system?
- A way of working / organizing / doing one or more tasks according to a fixed plan, program or set of rules.
- An arrangement in which all its units assemble and work together according to the plan / program / rules.

## Slide 7: SYSTEM EXAMPLE #1
WATCH
It is a time-display SYSTEM
Parts: Hardware, Needles, Battery, Dial, Chassis, Strap
Rules:
All needles move clockwise only
A thin needle rotates every second
A long needle rotates every minute
A short needle rotates every hour
All needles return to the original position after 12 hours
7

## Slide 8: SYSTEM EXAMPLE #2
WASHING MACHINE
It is an automatic clothes washing SYSTEM
Parts: Status display panel, Switches, Dials, Motor,
Power supply, Inner-water level sensor
Rules:
1.Wash clothes - spin
2.Rinse clothes
Dry clothes
Indicate “wash is over" by sound/blinking
Each step displays the process stage
If interrupted, execute only the remaining
8

## Slide 9: EMBEDDED SYSTEM
6
An Embedded System is one that has computer hardware with software embedded in it.
SOFTWARE PROGRAM
#include <18f84520.h>
#use delay (clock=20000000) #byte PORTB=6
main()
{
set_tris_b(0);
portb=255; //decimal
//hexadecimal
delay_ms(1000); portb=0x55; delay_ms(1000);
}
HARDWARE

## Slide 10: COMPUTER HARDWARE
Microprocessor
Memory
(Primary and Secondary)
(RAM, ROM and caches)
Input Units
(Keyboard, Mouse, Scanner, etc.)
Output Units
(Monitor, printer, etc.)
Networking Units
(Ethernet Card, Drivers, etc.)
I/O Units
(Modem, Fax cum Modem, etc.)

## Slide 11: EMBEDDED SYSTEM HARDWARE
Hardware
Processor, Timers, Interrupt controller, I/O Devices, Memories, Ports, etc.
Application Software
Software that performs the series of tasks or multiple tasks.
Real Time Operating System (RTOS)
It supervises the application software - sets the rules during the execution of the application programs.
A small scale embedded system may not need an RTOS.

## Slide 12: EMBEDDED SYSTEM BLOCK DIAGRAM

## Slide 14: EMBEDDED SYSTEM CONSTRAINTS
Embedded system software is designed to within
3 primary constraints:
Limited processor speed (kHz, MHz)
Low system memory (kB, MB)
Low power dissipation
When running the system continuously in cycles of wait for events, run, stop and wakeup.

## Slide 15
How are
EMBEDDED SYSTEMS
Different?
Real-time operation
Size
Cost
Reliability
Safety
Power
Security

## Slide 16: EMBEDDED SYSTEM CLASSIFICATIONS
Small Scale Embedded System
Medium Scale Embedded System
Sophisticated Embedded System

## Slide 17: SMALL SCALE EMBEDDED SYSTEM
Single 8-bit or 16-bit Microcontroller.
Low hardware and software complexity.
May be battery operated.
“C” is used for developing these system.
Programming tools:
Editor, Assembler and Cross-Assembler

## Slide 18: MEDIUM SCALE EMBEDDED SYSTEM
Single or few 16-bit or 3-bit microcontrollers or Digital Signal Processors (DSP) or Reduced Instructions Set Computers (RISC).
Medium hardware and software complexity.
Programming tools:
RTOS, Simulator, Debugger
Integrated Development Environment (IDE).

## Slide 19: SOPHISTICATED EMBEDDED SYSTEM
Enormous hardware and software complexity
May need scalable processor or configurable processor and programming logic arrays (PLAs).
Constrained by the processing speed available in their hardware units.
Programming Tools:
Advanced Software Development IDEs

## Slide 20: PROCESSOR
A Processor is the heart of the Embedded System.
For an embedded system designer knowledge of microprocessor and microcontroller is a must.
Two Essential Units: Control Unit (CU), Execution Unit (EU)
Operations Fetch Execute

## Slide 21: VARIOUS PROCESSOR
General Purpose processor (GPP)
Microprocessor Microcontroller Embedded Processor Digital signal Processor
Application Specific System Processor (ASSP)
Multi Processor System using GPPs

## Slide 22: MICROPROCESSOR
A microprocessor is a single chip semiconductor device, but not a complete computer.
Its CPU contains an ALU, a program counter, a stack pointer, some working register, a clock timing circuit and interrupt circuit on a single chip.
To make a complete computer, one must add memory usually ROM and RAM, memory decoder, an oscillator and a number of serial and parallel ports.

## Slide 23: MICROCONTROLLER
A microcontroller is a functional computer system-on-a-chip. It contains a processor, memory, and programmable input/output peripherals.
Microcontrollers include an integrated CPU, memory (a small amount of RAM, program memory, or both) and peripherals capable of input and output.

## Slide 24: VARIOUS MICROCONTROLLERS
INTEL
8031,8032,8051,8052,8751,8752
PIC
8-bit PIC16, PIC18
16-bit DSPIC33 / PIC24, PIC16C7x
Motorola
MC68HC11

## Slide 25: DIGITAL SIGNAL PROCESSOR
DSP is a single chip VLSI computeunit
Includes
Computational capabilities of microprocessor
and
Multiply & accumulate units (MAC)
Applications such as image processing, audio, video & telecommunication processing systems
It is used for fast signal processing functions
Examples : TMS320Cxx, SHARC, Motorola 5600xx, ADI Blackfin

## Slide 26: OTHER HARDWARE
Power Source
Clock Oscillator
Real Time Clock (RTC)
Reset Circuit, Power-up Reset and watchdog timer Reset
Memory
I/O Ports, I/O Buses
Interrupt Handler
DAC and ADC
LCD and LED Display
Keypad/Keyboard

## Slide 27: SOFTWARE
SIMULATORS
Masm
MPLAB
SOFTWARE
Assembly
C /C++
Dot Net
COMPILER
MC18 KEIL

## Slide 28: APPLICATIONS
Household appliances:
Microwave ovens, Television, DVD Players & Recorders
Audio players
Integrated systems in aircrafts and missiles
Cellular telephones
Electric and Electronic Motor controllers
Engine controllers in automobiles
Calculators
Medical equipments
Videogames
Digital musical instruments, etc.

## Slide 31
EMBEDDED AUTOMOTIVE SYSTEMS
Today’s high-end automobile may have 100 microprocessors
  4-bit microcontroller checks seat belt
  8-bit microcontrollers run dashboard devices
  16/32-bit microprocessor controls engine