## Slide 1: Digital Electronics
A gentle introduction!

## Slide 2: What is Digital Electronics ?
Electric Circuits which operate on / with "digital" signals
Uses binary notation (1’s and 0’s) for data transmission
Circuits are made of logic gates

## Slide 3: Basic Element: Transistor (switching mode)

## Slide 4: Transistor Mechanical Analogy
force – voltage/current water flow – current
- amplification

## Slide 5: Analog and Digital: Comparison

## Slide 6: Analog ↔ Digital: Conversion
ADC converts real-world analog data to digital form.
DAC converts digital data to continuous form

## Slide 7: Advantages of going Digital
Easy to design
Flexibility in programming
Immune to noise
High-speed designs possible
Transmission over long distances more secure

## Slide 8: Disadvantages of going Digital
Higher design cost
Less Portability
Higher energy consumption
Real world needs A-D conversions
Quantization errors due to sampling

## Slide 9: Number systems

## Slide 10: Decimal Number System
Uses 10 symbols / digits: 0,1,2,3,4,5,6,7,8,9
Base 10 (also called Decimal)
Natural number system for counting
  for humans
Read as:
  Three Thousand Six Hundred Eighty Seven
Decomposed as:

## Slide 11: Binary Number System
Uses 2 symbols / digits: 0,1
Base 2 (also called Binary)
Natural number system for counting
  for computers!
Read as:
  One Zero One One
Decomposed as:

## Slide 12: Hexadecimal Number System
Uses 16 symbols / digits: 0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F
Base 16 (also called Hexadecimal)
Natural system for expressing large numbers
  Like memory addresses in computers!
Read as:
  0x “One A Six D”
Decomposed as:
1 x 163 + 10 x 162 + 6 x 161 + 13 x 160
= 4096 + 2560 + 96 + 13 = 6765 (decimal)
0x1A6D

## Slide 13: Binary System Operations
Summation (add)
Subtraction (difference)
Multiplication
Division

## Slide 14: Binary Operation: Add

## Slide 15: Binary Operation: Subtract
Borrow -> 111
10100
- 111
-----------------
01101

## Slide 16: Binary Operation: Multiply

## Slide 17: Binary Operation: Divide

## Slide 18: logic Gates

## Slide 19: NOT gate
Symbol | Truth Table | 
 | X | Z
 | 0 | 1
 | 1 | 0

## Slide 20: OR gate
Symbol | Truth Table |  | 
 | X | Y | Z
 | 0 | 0 | 0
 | 0 | 1 | 1
 | 1 | 0 | 1
 | 1 | 1 | 1

## Slide 21: AND gate
Symbol | Truth Table |  | 
 | X | Y | Z
 | 0 | 0 | 0
 | 0 | 1 | 0
 | 1 | 0 | 0
 | 1 | 1 | 1

## Slide 22: NAND gate (UNIVERSAL)
Symbol | Truth Table |  | 
2-input NAND Gate | A | B | Q
 | 0 | 0 | 1
 | 0 | 1 | 1
 | 1 | 0 | 1
 | 1 | 1 | 0

## Slide 23: NOR gate
Symbol | Truth Table |  | 
2-input NOR Gate | A | B | Q
 | 0 | 0 | 1
 | 0 | 1 | 0
 | 1 | 0 | 0
 | 1 | 1 | 0

## Slide 24: XOR gate
Symbol | Truth Table |  | 
2-input XOR Gate | A | B | Q
 | 0 | 0 | 0
 | 0 | 1 | 1
 | 1 | 0 | 1
 | 1 | 1 | 0

## Slide 25: Ex-OR / XOR gate: Insight

## Slide 26
Ex-OR / XOR gate: Insight

## Slide 27: Combinational Logic
Output depends
  only on current inputs
Previous inputs do not have any effect
We call it memoryless system
Examples:
  All logic gates studied so far
    NOT gate
    OR gate
    AND gate
    NAND gate
    NOR gate
    XOR gate

## Slide 28: Sequential Logic
Output depends
  not only on current inputs but also on past sequence of inputs
We say it possesses memory
Output depends on a sequence of events occurring at inputs
Examples: Latch, Flip-Flop

## Slide 29: Latch Example: SR
Set Reset (SR) Latch
R==1 ‘resets’ Q, S==1 ‘sets’ Q
S==R==1 is invalid
No clock / synchronization
Remember for NAND
  1,1 gives 0
  All others give 1
S | R | S’ | R’ | Q | Q’
0 | 0 | 1 | 1 | Qprev | Q’prev
0 | 1 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | Inv | Inv

## Slide 30: Flip Flop Example: SR
Set Reset (SR) Flip Flop
  notice the CLK
S==1 ‘sets’, R==1 ‘resets’
  But only when CLK is high
CLK | S | R | Q | Q’
↑ » 1, ↓ » 0 | 0 | 0 | 0 | 1
↑ » 1, ↓ » 0 | 0 | 1 | 0 | 1
↑ » 1, ↓ » 0 | 1 | 0 | 1 | 0
↑ » 1, ↓ » 0 | 1 | 1 | X | X

## Slide 31: Flip Flop Example: D
D Flip Flop
  notice the CLK
“Delays” the signal through CLK
CLK | D | Q | Q’
↓ » 0 | 0 | 0 | 1
↑ » 1 | 0 | 0 | 1
↓ » 0 | 1 | 0 | 1
↑ » 1 | 1 | 1 | 0

## Slide 32: Boolean Algebra
Mathematics / Algebra of Digital Signals
Limited operations possible:
  OR (X + Y)
  AND (X . Y)
  NOT (~ X)
DeMorgan’s Laws help in simplification

## Slide 33: Integrated Circuit (IC)
A set of electronic circuits on one small flat piece (or "chip") of semiconductor material, normally silicon.

## Slide 34: ICs: Classification
Acronym | Expanded form | Year | # of transistors | # of logic gates
SSI | small-scale integration | 1964 | 1 to 10 | 1 to 12
MSI | medium-scale integration | 1968 | 10 to 500 | 13 to 99
LSI | large-scale integration | 1971 | 500 to 20,000 | 100 to 9,999
VLSI | very large-scale integration | 1980 | 20,000 to 1,000,000 | 10,000 to 99,999
ULSI | ultra-large-scale integration | 1984 | 1,000,000 and more | 100,000 and more

## Slide 35: IC Families
Family refers to the type of elements / devices used for creating the Digital Circuit
There are several IC Families:
  TTL (Transistor-Transistor Logic)
  CMOS (Complementary Metal Oxide Semiconductor)
  ECL (Emitter-Collector Logic)
  etc.
Each Family has its own properties and parameters
  These play a big role in selecting a Family for an Application

## Slide 36: IC Family Parameters
Power Supply Voltage
Operating Temperature
  Minimum, Maximum
Propagation Time
Noise Immunity
Power Dissipation
Fan-in
Fan-out

## Slide 37: IC Family: TTL
Supply Voltage
  4.5 – 5.5 V
Operating Temperature
  0 – 70ºC
Transition zone
  1 – 1.5V
Propagation Time
  10 nsec
Power Dissipation
  ~10mW/gate

## Slide 38: IC Family: CMOS
Supply Voltage
  Variable, 3 – 15 V
Operating Temperature
  0 – 85ºC
Transition zone
  2.25 – 2.75V (noise immunity)
Propagation Time
  125 nsec (5V), 45nsec (15V)
Power Dissipation
  ~10nW/gate

## Slide 39: Thank you!