## Slide 1: The PIC microcontroller
PIC18F4520: Introduction, Architecture

## Slide 2: Embedded System
  A system whose principal function is
  not computational
  but which is
  controlled by an embedded computer

## Slide 3: Microprocessors vs Microcontrollers
Microprocessor: processor on one silicon chip.
Microcontroller: microprocessor with added circuitry
Thus microprocessor is a sub-set of microcontroller
Intel Microprocessor vs PIC Microcontroller
Intel is more complex, costs more, is more powerful
PIC is less costly, less complex, far less powerful
Paradox: How come Intel is a sub-set of PIC!

## Slide 4: Microcontroller Internals

## Slide 5: Example: Autonomous Guided Vehicle

## Slide 6: Human Locomotion: Basics
Need for motion
  Go from point A to point B
Sense the environment
  Using “sensors” – eyes, ears, nose, skin
Chart possible paths
  Assess risk, choose the best path
Actuate the “moving engine”
  Start moving legs – in walking / running / creeping / crouching pose
Keep sensing the environment for “changes”
  Respond to changes
  Assess risk
  Keep “moving”

## Slide 7: Machine locomotion: Comparison
Human locomotion
Need for motion
Sense the environment
Chart possible paths
Actuate the “engine”
Keep sensing
  Respond to changes
Machine locomotion
Need for motion
  Robotic movement problem
Sense the environment
  camera, sonar, lidar, radar
Chart possible paths
  Path planning algorithms
Actuate the “engine”
  “motors” – speed, direction
Keep sensing
  Respond to changes - bump

## Slide 8: Autonomous Guided Vehicle: Internals

## Slide 9: Microcontroller Family – the concept

## Slide 10: Microcontroller Packaging, Appearance
From left to right: PIC 12F508, PIC 16F84A, PIC 16C72, Motorola 68HC05B16, PIC 16F877, Motorola 68000

## Slide 11: PIC Microcontrollers - history
Peripheral Interface Controller (PIC) was originally designed by General Instruments
In the late 1970s, GI introduced PIC1650 and PIC1655 – RISC with 30 instructions
PIC was sold to Microchip
  Microchip today ends up making most of the 8-bit PICs
We are studying the PIC18F family controller
  Features: low-cost, self-contained, 8-bit, Harvard structure, pipelined, RISC, single accumulator, with fixed reset and interrupt vectors

## Slide 12: PIC Family: Development history
PIC Family | Stack Size | Instruction Word Size | No of Instructions | Interrupt Vectors
12CX/12FX | 2 | 12- or 14-bit | 33 | None
16C5X/16F5X | 2 | 12-bit | 33 | None
16CX/16FX | 8 | 14-bit | 35 | 1
17CX | 16 | 16-bit | 58 | 4
18CX/18FX | 32 | 16-bit | 75 | 2
‘C’ implies CMOS technology; Complementary Metal Oxide Semiconductor
‘F’ insert indicates incorporation of Flash memory technology

## Slide 13: PIC18F4520: Pin-out

## Slide 14: PIC18F4520: Pin-out observations
Almost all pins are “multi-functional”
  A / B / C
    eg. OSC1 / CLKI / RA7 (pin 13)
  Lowers cost – by driving down “pin real-estate”
  Assumption: You may not need all 2/3 functions on a pin at once
PIC is a soft-configured controller
  Pin function is decided by software (code)
The only pins which are not multi-functional
  Vdd, Vss

## Slide 15: PIC18F: Controller Architecture

## Slide 16: PIC: Program data flow
“Controller Bus”
“FREG”
“WREG”

## Slide 17: What are PIC instructions like?
Type 1
  Data comes along with the instruction
    Example: ADDLW 0x20
Type 2 – unified address space
  Data comes from file registers
    Internal RAM
      Example: ADDWF 0x20
    External (real-world) peripheral
      Example: ADDWF PORTA
Type 3
  Data comes from “pointer” file-registers (FSRs)
    Example: ADDWF INDF0

## Slide 18: PIC18F ALU: It’s different!

## Slide 19: PIC18F: ALU – how different?
Regular ALU
Result = Input1 (Operation) Input2
PIC18F ALU
Result = [WREG] (Operation) Input2

## Slide 20: PIC18F ALU: Details
Arithmetic and Logical Instructions
  Add, Subtract, Multiply
  And, Or, Not, Shift, Rotate
Single Accumulator
  Called WREG (working register)
Feedback loop for input
  W is one input – by default
Two options for destination
  Output does not necessarily go to the Accumulator (WREG)
  Output options:
    WREG, FREG
  Called Destination Control in PIC
  Each ALU instruction has the ability to redirect output

## Slide 21: PIC18F4520: Clocking options
PIC can accept several different clock inputs:
  External clock – crystal oscillator module
  Self-oscillating with external crystal or ceramic resonator
  External or self-oscillating with external Phase Locked Loop (PLL)
  Self-oscillating with external RC
Set up using configuration bits
PIC supports variable operating frequency
  Within defined limits
  Ranges from kHz to MHz
  Depends on external clocking mechanism used

## Slide 22: PIC18F4520: Peripherals
Data Ports (Digital)
  Port A, B, C, D (8-bits each), E (4-bit)
Timer / Counter modules
  Timer0 (8-bit), Timer1 (16-bit), Timer2 (8-bit), Timer3 (16-bit)
CCP/PWM modules
  CCP as well as ECCP
Serial ports
  USART (RS-232)
  I2C, SPI (both buses – Master, Slave modes)
ADC – 10-bit resolution
  13 input channels (with 13-way input multiplexer)
256-byte EEPROM – configuration info

## Slide 23: PIC18F4520: Reset Circuitry
Multiple “resets” in hardware:
  Power On Reset
  Hardware Pin (External) Reset – MCLR’ (active low)
  Brown Out Reset – Power Supply Voltage
    BOR tolerance level is configurable in software (5V / 3.3V)
  Watchdog Timer Reset
Startup delays
  Power Up timer (72ms delay)
  Startup Timer (1024 Oscillator cycles)
Software (code) can also perform a reset
Reset flushes RAM and makes PIC ‘boot’ from starting location of code (0x00000)

## Slide 24: PIC18F4520: So many resets?
Most embedded circuits / systems:
  Are tiny
  Have no human interactions
  Are numerous
  Are ill-located for human access
  Are supposed to be auto-fail-safe
This explains the need for “resets” to handle various scenarios
  But how does a reset solve the issue at hand??

## Slide 25: Programming: Stack concept
Every CPU has a Program Counter (PC)
  Keeps track of which instruction to execute next
Usually, instructions execute “sequentially”
  One after another – so PC increments
But if there is a function call or interrupt
  Sequential flow is “disturbed”
  For function calls, CPU “jumps” to the location of the function code
    And then has to jump back (after the function “returns”)
    We need to remember the address from where we jumped
      This is stored in the Stack

## Slide 26: PIC18F: Program flow with stack

## Slide 27: PIC18F: Stack details
Stack organization
Stack usage
Function_1()
  Function_2()
    Function_3()
“Nested” functions
Limit to nesting!
  31 levels

## Slide 28: PIC18F: Memories
Separate Memory Regions:
  Code / Program – Non-volatile memory (NAND Flash)
    Holds program / instructions
  Data – Volatile memory (RAM)
    Holds run-time data
Address Spaces are different
  Though the range “overlaps”
    eg. 0x10 could be a code address as well as a data address!
We need to be specific about which memory are we talking about!

## Slide 29: PIC18F: Code memory map
Non-volatile
Range:
  0x0000 to 0x7FFF (32k)
Each location contains 1 instruction
3 special addresses:
  0x0000
  0x0008
  0x0018

## Slide 30: PIC18F: Data memory map
Volatile memory
Range:
  0x000 to 0xFFF
Each location is 8-bits
  Also called FREG
  Has an address eg. 0x020
Bank: 256-byte chunk
  Top bank: GPR0
  Bottom bank: SFR
Only SFR and any 1 GPR active at a time
8 bits
0x000
0x001

## Slide 31: Programming: Why bank data?
Programmers typically use variables for computing
  eg. x + y = z
  How many variables can the human mind keep track of?
1 Bank is 0x100 – 256 bytes – 256 possible variables
  1 bank is more than enough for “our” programming needs
Compilers (higher-level languages like C) need many more variables
  Remember: int a, float b, char c[20];
  They end up using multiple banks
    By using “bank switching”
Most real-world projects are a combination of C and hand-coded (optimized) assembly-code

## Slide 32: PIC18F: SFR data bank
Special Function Register (SFR) bank
Each location is 8-bits
  Also called FREG
  Has address as well as “label”/”name”
  eg. PORTA, WREG
They fulfill important functions
  WREG
  Peripherals (IO Ports)
  Counters/Timers
Always active data bank

## Slide 33: PIC 8-bit family data banking
PIC18F has 6 data banks “populated”
  GPR0 to GPR5
Higher addresses are “unused” (bank 6+)
    Address exists but no physical memory
Inter-family code portability

## Slide 34: Programming: Instruction set
Microcontrollers:
  Being computers, only understand binary / digital
Difficult for humans to talk digital
Solution:
  Assembly language
    Mnemonic based ‘English-like’ language
  Called instruction set
  eg. ADD A, B ≡ ADD A and B together and give me the result
Every microcontroller has its own instruction set
  It’s ‘mother tongue’
  An “assembler” converts assembly to binary

## Slide 35: PIC 8-bit family: Instruction set
PIC is a RISC chip ≡ less number of instructions
Most instructions execute in:
  1 instruction cycle ≡ 4 Clock cycles
Thus:
  PIC running at 40 MHz can run 10 M instructions
  PIC running at 40 KHz can run ??
Family | # of instructions | Instruction size
PIC16 | 35 | 14 bits
PIC18 | 59 | 16 bits
PIC24 | 71 | 24 bits

## Slide 36: PIC18: Assembly
Assembly language instruction format
[label] [mnemonic] [operands] [;comment]
Assembler directives
  ORG
  EQU/SET
  LIST
  END
  #include
  _config
  radix

## Slide 37: PIC18F: An assembly ‘program’
#include “P18F4520.inc”
MY_VAR EQU 0x01 ; create a label for 0x01
ORG 0x0
ADDLW 0x07
ADDLW MY_VAR ; MY_VAR is 0x01
LABEL1 ADDLW 0x06
GOTO LABEL1 ; loop back!
END

## Slide 38: PIC18F: Instruction set grouping

## Slide 39: PIC18F: Instruction examples
Byte-oriented file-register operations
  MOVWF, ADDWF, CLRF, DECF
Bit-oriented file-register operations
  BCF, BTFSC
Control operations
  BRA, BNZ, CALL, RETURN
Literal instructions
  MOVLW, ADDLW

## Slide 40: Thank you!