## Slide 1: The PIC microcontroller
PIC18F4520: Instruction Set – Part 1

## Slide 2: PIC18F: Controller Architecture

## Slide 3: PIC18F: Instruction set grouping

## Slide 4: PIC18F: Notational convention
WREG
  W Register
FREG
  File Register (any register location from GPR Bank 0 / SFR)
[X]
  Contents of register X
  Examples:
    [WREG] = 0x02 ↔ WREG’s contents become 0x02
    [0x20] = 0x34 ↔ RAM File Register 0x20 content becomes 0x34
    [X] = [Y] ↔ Contents of Y are copied into X

## Slide 5: Byte-oriented instructions

## Slide 6: PIC18F: Instructions – byte-oriented move
Move operations – data movement / copy
  MOVLW 0x20
    Move 0x20 into WREG
      Effect: [WREG] = 0x20
  MOVWF 0x20
    Move [WREG] to 0x20
      Effect: [0x20] = [WREG]
0x--
WREG
0x20
WREG
0x23
WREG
0x--
0x20
0x--
0x21
GPR0
0x23
WREG
0x23
0x20
0x--
0x21
GPR0

## Slide 7: PIC18F: Instructions – register set/clear
SETF
  Set all bits of FREG to 1
  Example: SETF 0x20
    Effect: [0x20] = (1111 1111)2 = (255)10 = 0xFF
CLRF
  Clear all bits of FREG
  Example: CLRF 0x20
    Effect: [0x20] = (0000 0000)2 = (0)10 = 0x00
0x--
0x20
0xFF
0x20
0x--
0x20
0x00
0x20

## Slide 8: PIC18F: Instructions – byte-oriented add
Add operations
  ADDLW 0x20
    Add 0x20 to WREG
      Effect: [WREG] = [WREG] + 0x20 = 0x11 + 0x20 = 0x31
  ADDWF 0x20
    Add [WREG] and [0x20]
      Effect: RESULT = [WREG] + [0x20]
0x11
WREG
0x42
0x20
0x--
0x21
GPR0
0x??
WREG
0x??
0x20
0x--
0x21
GPR0
RESULT = 0x11 + 0x42 = 0x53
0x11
WREG
0x31
WREG

## Slide 9: PIC18F ALU: Connections

## Slide 10: PIC18F: Destination Control
ALU result destination: Either WREG or FREG
Indicated by destination flag at the instruction’s end
  Example: ADDWF 0x20, F => Destination is FREG (0x20)
  Example: ADDWF 0x20, W => Destination is WREG
0x11
WREG
0x42
0x20
0x--
0x21
GPR0
0x11
WREG
0x53
0x20
0x--
0x21
GPR0
0x11
WREG
0x42
0x20
0x--
0x21
GPR0
0x53
WREG
0x42
0x20
0x--
0x21
GPR0

## Slide 11: PIC18F: Playing with destination control
MOVLW 0x10
MOVWF 0x20
MOVLW 0x30
ADDWF 0x20,W
ADDWF 0x20,F
[WREG] = 0x10
[0x20] = 0x10
[WREG] = 0x30
[WREG] = ?
[0x20] = ?
[WREG] = ?
[0x20] = ?
MOVLW 0x10
MOVWF 0x20
MOVLW 0x30
ADDWF 0x20,F
ADDWF 0x20,W
[WREG] = 0x10
[0x20] = 0x10
[WREG] = 0x30
[WREG] = ?
[0x20] = ?
[WREG] = ?
[0x20] = ?

## Slide 12: PIC18F: More byte-oriented instructions
Data movement
  MOVF
  MOVFF
Arithmetic
  ADDWFC
  SUBWF, SUBWFB
  SUBFWB
Logical
  ANDWF, IORWF, XORWF

## Slide 13: PIC18F: Instructions – more moves
MOVF 0x20, W
  Move contents of 0x20 into WREG
MOVFF 0x20, 0x40
  Move content of 0x20 to 0x40
0x--
WREG
0xAB
0x20
0x--
0x21
GPR0
0xAB
WREG
0xAB
0x20
0x--
0x21
GPR0
0x--
0x40
0x--
0x41
GPR0
0xCD
0x40
0x--
0x41
GPR0
0xCD
0x20
0x--
0x21
0xCD
0x20
0x--
0x21

## Slide 14: PIC18F: Instructions – add overflow
What if ADDWF results in overflow (a carry)?
  Example: ADDWF 0x20, where [WREG] = 0xFF, [0x20] = 0x02
  1
  0xFF
  + 0x02
  ---------
  0x101
  Result = 0x101 (257)10 : greater than 8-bits!
    Where does the extra 1 go?
  It goes into the CARRY bit of the STATUS REGISTER
  Final Result = 0x01, Carry bit = 0x1
  Hexadecimal add:
  0xF + 0x1 = 0x10
  0xF + 0x2 = 0x11

## Slide 15: PIC18F ALU: Status Register
C = Carry bit for addition, borrow bit for subtraction

## Slide 16: PIC18F: Instructions - add with carry
To ensure CARRY bit is taken care of:
ADDWFC (ADDWF with Carry)
  Example: ADDWFC 0x20 for [WREG] = 0x01, [0x20] = 0x02, C = 1
  0x01 [WREG]
  +0x02 [0x20]
  +0x01 [Carry bit]
  --------
  0x04 Result
  Note: ADDWFC uses CARRY bit from previous operation

## Slide 17: Mathematics: Addition, Subtraction
Addition:
  a + b = b + a
  Hence, addition is called commutative – order does not matter
  So an ADDWF / ADDWFC suffices
Subtraction
  a – b ≠ b – a
  Thus, subtraction is non-commutative – order does matter!
  So, PIC18F has separate instructions for (a-b) and (b-a)!
    SUBWFB and SUBFWB

## Slide 18: PIC18F: Instructions - subtraction
SUBLW (subtraction with W)
  Example: SUBLW 0x20
  Effect: [WREG] = 0x20 – [WREG]
SUBWF (plain subtraction)
  Example: SUBWF 0x20, F
  Effect: [0x20] = [WREG] – [0x20]
SUBWFB (subtraction with borrow)
  Example: SUBWFB 0x20, F
  Effect: [0x20] = [WREG] – [0x20] – C (Borrow flag)
SUBFWB (reverse subtraction with borrow)
  Example: SUBFWB 0x20, F
  Effect: [0x20] = [0x20] – [WREG] – C (Borrow flag)

## Slide 19: Mathematics: Multiplication
Multiplication:
  a * b = b * a
  Hence, multiplication is commutative – order does not matter
The problem with multiplication – overflow!
  8-bit number * 8-bit number
    Gives a 16-bit answer – product
    Example: 255 * 255 = 28 * 28 = 2(8+8) = 216 = 65036
    Can’t fit in any 8-bit register
    Hence, the need for a register pair PRODH:PRODL

## Slide 20: Mathematics: Division
Division:
  a / b ≠ b / a
  Hence, division is non-commutative – order does matter!
But division is much more complicated!
  Corner cases
    1 / 2 → Decimal fraction (0.50)
    1 / 3 → Repeating decimal fraction(0.33333…)
    1 / 7 → Repeating decimal sequence fraction (0.142857142857…)
    1 / 0 → ∞
    0 / 0 → ?
Certainly not fixed-point!

## Slide 21: PIC18F: Instructions - multiplication
MULLW (multiplication with W)
  Example: MULLW 0xFF for [WREG] = 0xFF
  Effect: [PRODH]:[PRODL] = [WREG] * 0xFF
  Result: 0xFF * 0xFF = 255 * 255 = 65025 = 0xFE01
0xFF
WREG
0xFE
PRODH
0x01
PRODL
SFR

## Slide 22: PIC18F: Instructions - multiplication
MULWF (multiplication with FREG)
  Example: MULWF 0x20 for [WREG] = 0x02, [0x20] = 0x01
  Effect: [PRODH]:[PRODL] = [WREG] * [0x20]
0x02
WREG
0x01
0x20
0x--
0x21
GPR0
0x00
PRODH
0x02
PRODL
SFR
  Result: 0x02 * 0x01 = 0x0002

## Slide 23: Logical instructions

## Slide 24: PIC18F: Instructions – logical AND(L)
ANDLW
  8-bit AND of [WREG] and Data
  Example: ANDLW 0x12 for [WREG] = 0x02
  0000 0010 [WREG]
  0001 0010 0x12
  --------------
  0000 0010 Result, goes into WREG
  Effect: [WREG] = 0x02

## Slide 25: PIC18F: Instructions – logical AND(F)
ANDWF
  8-bit AND of [WREG] and [FREG]
  Example: ANDWF 0x20, F for [WREG] = 0x02, [0x20] = 0x12
  0000 0010 [WREG]
  0001 0010 [0x20]
  --------------
  0000 0010 Result, goes into 0x20
  Effect: [0x20] = 0x02

## Slide 26: PIC18F: Instructions – logical OR(L)
IORLW
  8-bit inclusive OR of [WREG] and Data
  Example: IORLW 0x12, F for [WREG] = 0x02
  0000 0010 [WREG]
  0001 0010 0x12
  --------------
  0001 0010 Result, goes into WREG
  Effect: [WREG] = 0x12

## Slide 27: PIC18F: Instructions – logical OR(F)
IORWF
  8-bit inclusive OR of [WREG] and [FREG]
  Example: IORWF 0x20, F for [WREG] = 0x02, [0x20] = 0x12
  0000 0010 [WREG]
  0001 0010 [0x20]
  --------------
  0001 0010 Result, goes into 0x20
  Effect: [0x20] = 0x12

## Slide 28: PIC18F: Instructions – logical XOR(L)
XORLW
  8-bit exclusive OR of [WREG] and Data
  Example: XORLW 0x12, F for [WREG] = 0x02
  0000 0010 [WREG]
  0001 0010 0x12
  --------------
  0001 0000 Result, goes into WREG
  Effect: [WREG] = 0x10

## Slide 29: PIC18F: Instructions – logical XOR(F)
XORWF
  8-bit exclusive OR of [WREG] and [FREG]
  Example: XORWF 0x20, F for [WREG] = 0x02, [0x20] = 0x12
  0000 0010 [WREG]
  0001 0010 [0x20]
  --------------
  0001 0000 Result, goes into 0x20
  Effect: [0x20] = 0x10

## Slide 30: PIC18F: Journey so far
Move
  MOVLW, MOVWF, MOVF, MOVFF
Register setup
  SETF, CLRF
Arithmetic (with and without carry/borrow)
  ADDLW, ADDWF, ADDWFC
  SUBLW, SUBWF, SUBWFB, SUBFWB
  MULLW, MULWF
Logical
  ANDLW, ANDWF
  IORLW, IORWF
  XORLW, XORWF

## Slide 31: Number crunching instructionS!

## Slide 32: PIC18F: Some more instructions!
Negation
  COMF
  NEGF
Rotate / Shift
  RLCF, RLNCF
  RRCF, RRNCF
Swap
  SWAPF
Increment, Decrement
  INCF, DECF

## Slide 33: PIC18F: Instructions - negation
COMF Binary complement (1→0, 0→1) of FREG’s content Also called one’s complement Example: COMF 0x20, F for [0x20] = 0x32 0x3 0x2 0xC 0xD 0011 0010 becomes 1100 1101 Result: [0x20] = 0xCD
NEGF Negation: Take the two’s complement of contents of FREG Example: NEGF 0x20, F for [0x20] = 0x32 0x3 0x2 0xC 0xE 0011 0010 becomes 1100 1110 Result: [0x20] = 0xCE

## Slide 34: PIC18F: Instructions – rotate left
RLCF
  Rotate Left with Carry bit the contents of FREG
  Example: RLCF 0x20, F for [0x20] = 0x20, C = 1
  C=1 becomes C=0
  0010 0000 0100 0001
  Result: [0x20] = 0x41
RLNCF
  Rotate Left with No Carry bit the contents of FREG
  Example: RLNCF 0x20, F for [0x20] = 0x20, C = 1
  C=1 becomes C=1
  0010 0000 0100 0000
  Result: [0x20] = 0x40

## Slide 35: PIC18F: Instructions – rotate right
RRCF
  Rotate Right with Carry bit the contents of FREG
  Example: RRCF 0x20, F for [0x20] = 0x20, C = 1
  C=1 becomes C=0
  0010 0000 1001 0000
  Result: [0x20] = 0x90
RRNCF
  Rotate Right with No Carry bit the contents of FREG
  Example: RRNCF 0x20, F for [0x20] = 0x20, C = 1
  C=1 becomes C=1
  0010 0000 0001 0000
  Result: [0x20] = 0x10

## Slide 36: Mathematics: Rotate/Shift for power of 2
What does shift right/left mean? Let’s take 4 (power of 2)
For 1-bit shift:
For 2-bit shift:
For n-bit shift:
 | Binary | Decimal
Original | 0100 | 4
Shift left by 1-bit | 1000 | 8
Shift right by 1-bit | 0010 | 2
Shift left ≡ “multiply by 2” | Shift right ≡ “divide by 2”
Shift left ≡ multiply by 4 (22) | Shift right ≡ divide by 4 (22)
Shift left ≡ multiply by 2n | Shift right ≡ divide by 2n

## Slide 37: PIC18F: Instructions – swap
Digital definitions
  Thus, 1 byte = 2 nibbles = 8 bits
SWAPF
  Swap the nibble contents of FREG
  Example: SWAPF 0x20, F for [0x20] = 0x34
  0011 0100 becomes 0100 0011
  Result: [0x20] = 0x43
Bit | Nibble | Byte
1-bit | 4-bits | 8-bits

## Slide 38: PIC18F: Instructions – add/subtract 1
INCF
  Increment (add 1) to contents of FREG
  Example: INCF 0x20, F for [0x20] = 0x12
  Effect: [0x20] = 0x12 + 0x01 = 0x13
DECF
  Decrement (subtract 1) from contents of FREG
  Example: DECF 0x20, F for [0x20] = 0x12
  Effect: [0x20] = 0x12 – 0x01 = 0x11
Preferred instructions for loops and counters

## Slide 39: PIC18F: Concept of “skip”
Skip means
  Jump over next instruction
Usually conditional
  If condition is TRUE
    Perform the skip
  Else
    Do not perform the skip
Leads to compact code
Code memory
If skip is not performed
  Execute n, n+1, etc
If skip is performed
  Execute n, then n+2
  n+1 not executed
Skip instn.
Instruction n
Instruction n+1
Instruction n+2

## Slide 40: PIC18F: Skip conditions
Example conditions for skips
  Zero flag – most popular
    SZ (skip if zero) SNZ (skip if not zero)
    Instructions: INCFSZ, DECFSZ INFSNZ, DCFSNZ
  Equality based
    SEQ (skip if equal), SGT (skip if greater than), SLT (skip if less than)
    Instructions: CPFSEQ, CPFSGT, CPFSLT
  Bit condition based
    SC (skip if clear), SS (skip if set)
    Instructions: BTFSC, BTFSS

## Slide 41: PIC18F: Instructions – skipful DEC
DECFSZ
    Decrement FREG contents
    Save the result
    Skip next instruction if result of increment is zero
DECFSZ 0x20, F
  Case 1: [0x20] = 0x05
    Result: [0x20] = ?
  Case 2: [0x20] = 0x01
    Result: [0x20] = ?
Code memory
Execution sequence:
  Case 1:
    ??
  Case 2:
    ??
DECFSZ 0x20, F
MOVLW 0x0
SUBWF 0x30, W
Instruction n
Instruction n+1
Instruction n+2

## Slide 42: PIC18F: Instructions – skipful INC
INFSNZ
    Increment FREG contents
    Save the result
    Skip next instruction if result of increment is not 0
INFSNZ 0x20, F
  Case 1: [0x20] = 0x10
    Result: [0x20] = ?
  Case 2: [0x20] = 0xFF
    Result: [0x20] = ?
Code memory
Execution sequence:
  Case 1:
    ??
  Case 2:
    ??
INFSNZ 0x20, F
MOVLW 0x0
SUBWF 0x30, W
Instruction n
Instruction n+1
Instruction n+2

## Slide 43: Bit-oriented instructions

## Slide 44: Industry: Motivation for bit-wise instruction
Lower pin count:
  Pin real estate in the embedded world is expensive
  Low-end devices (sensors) come in 1/2/3-pin forms
Using a byte is overkill
  Hardware – pin level
    Why waste an 8-pin port for interacting with a 1/2/3 pin sensor?
  Hardware – register-level
    Why use an 8-bit register when you need less bits?
  Software – code level
    Why use a byte-oriented instruction
      When you could do with a bit-oriented one?!

## Slide 45: PIC18F: Instructions – bit-wise, simple
Syntax: Bxx FREG, n (0 ≤ n ≤ 7)
BSF
  Bit Set – set a particular bit in an FREG
  Example: BSF 0x20, 0 for [0x20] = 0x12
  Result: [0x20] = 0001 0011 = 0x13
BCF
  Bit Clear – clear a particular bit in an FREG
  Example: BCF 0x20, 4 for [0x20] = 0x12
  Result: [0x20] = 0000 0010 = 0x02
0001 0010
0x20
0x20
0001 0011
0001 0010
0x20
0x20
0000 0010

## Slide 46: PIC18F: Instructions – bit-wise, simple
BTG
  Bit toggle – toggle a particular bit in an FREG
  Example: BTG 0x20, 3 for [0x20] = 0x12
Point to note in bit-wise instructions:
  Only the bit mentioned is affected
  Other bits stay as they are!
0001 0010
0x20
0x20
0001 1010
  Result: [0x20] = 0001 1010 = 0x1A

## Slide 47: PIC18F: Instructions – bit-wise, skipful (S)
BTFSS FREG, n
  Bit Test FREG’s nth bit
  Skip if it is Set
BTFSS 0x20, 0
Case 1: [0x20] = 0x01
  0000 0001
Case 2: [0x20] = 0x00
  0000 0000
Code memory
Execution sequence:
  Case 1:
    ??
  Case 2:
    ??
BTFSS 0x20, 0
MOVLW 0x0
SUBWF 0x30, W
Instruction n
Instruction n+1
Instruction n+2

## Slide 48: PIC18F: Instructions – bit-wise, skipful (C)
BTFSC FREG, n
  Bit Test FREG’s nth bit
  Skip if it is Clear
BTFSC 0x20, 0
Case 1: [0x20] = 0x01
  0000 0001
Case 2: [0x20] = 0x00
  0000 0000
Code memory
Execution sequence:
  Case 1:
    ??
  Case 2:
    ??
BTFSC 0x20, 0
MOVLW 0x0
SUBWF 0x30, W
Instruction n
Instruction n+1
Instruction n+2

## Slide 49: PIC18F: Journey so far
Negation
  COMF, NEGF
Rotate / shift
  RLCF, RLNCF, RRCF, RRNCF
Swap
  SWAPF
Increment, decrement (with and without skip)
  INCF, DECF
  INCFSZ, INFSNZ, DECFSZ, DCFSNZ
Bit-oriented (with and without skip)
  BSF, BCF, BTG
  BTFSS, BTFSC

## Slide 50: PIC18F: Instructions – Part 1 summary
Move
Setup
Arithmetic
Logical
Negation
Rotate-shift
Swap
Concept of skip
Increment / decrement
Bit-oriented

## Slide 51: Thank you!