## Slide 1: The PIC microcontroller
PIC18F4520: Instruction Set – Part 2

## Slide 2: PIC18F: Controller Architecture

## Slide 3: PIC18F: Instruction set grouping

## Slide 4: PIC18F: Notational convention
WREG
  W Register
FREG
  File Register (any register location from GPR Bank 0 / SFR)
[X]
  Contents of register X
    [WREG] = 0x02 ↔ WREG’s contents become 0x02
    [0x20] = 0x34 ↔ RAM File Register 0x20 content becomes 0x34
    [X] = [Y] ↔ Contents of Y are copied into X
Number systems
Decimal | d’10’
Hexadecimal | h’4A’ or 0x4A
Binary | b’1000 0010’

## Slide 5: control instructions

## Slide 6: Programming: Concept of branch
Usually, program flow is sequential
  Instructions execute one after another in sequence
    Effect: [PC] = [PC] + <size_of_instruction>
In certain scenarios, we may want to break this sequence
  Unconditional jumps
  Conditional jumps
  Function / sub-routine calls (and returns)
  Interrupts / urgency
This disturbance of sequentiality is called branching
  The controller is said to have branched off
  Instruction execution continues from a different point in the code
    Effect = [PC] ≠ [PC] + <size_of_instruction>

## Slide 7: PIC18F: Branching - unconditional
GOTO
  Go To the label mentioned
    This label must exist somewhere in the code!
  Example: Consider the code snippet
  …
  MOVLW 0x0
  GOTO LABEL1
  ADDWF 0x20
  SUBWF 0x30
  LABEL1 CLRF 0x20
  SETF 0x40
  …
GOTO is a 4-byte instruction with 20-bits for jump-address
  Called Long Jump
  Jump range: Anywhere within code-space

## Slide 8: PIC18F: Branching - unconditional
BRA
  Branch to the label mentioned
    This label must exist somewhere in the code!
  Example: Consider the code snippet
  …
  MOVLW 0x0
  BRA LABEL1
  ADDWF 0x20
  SUBWF 0x30
  LABEL1 CLRF 0x20
  SETF 0x40
  …
BRA is a 2-byte instruction with 11-bits for jump-address
  Called Short Jump
  Jump range: ± 210 : -1023 to +1024

## Slide 9: PIC18F: Branching – conditional
Conditions for branching:
  Zero flag
    BZ, BNZ
  Carry flag
    BC, BNC
  Negative flag
    BN, BNN
  Overflow flag:
    BOV, BNOV
Most popular, intuitive: zero-flag based branching (BZ, BNZ)
All conditional branches are 2-byte instructions
  1-byte for jump address
  Short jumps, range: -127 to +128

## Slide 10: PIC18F: Branching – conditional (Z/NZ)
BZ
  Branch if zero flag is set – result of previous ALU operation is 0
  Example: Consider the code snippet
  …
  DECF 0x20 Zero flag will be set if result is 0
  BZ LABEL1
  MOVLW 0x00
  MULLW 0x30
  CLRF 0x16
  LABEL1 ADDWF 0x01
  SETF 0x30 After DECF:
  … Case 1: [0x20] ≠ 0x0
  Case 2: [0x20] = 0x0
BNZ
  Branch if not zero

## Slide 11: PIC18F: Journey so far
Unconditional jumps
  GOTO
  BRA
Conditional jumps
  BZ, BNZ
  BC, BNC
  BN, BNN
  BOV, BNOV

## Slide 12: PIC18F: An exercise in coding!
Problem statement
  To an initialized WREG, add 4, 5 times
Mental exercise
  Start with WREG = 0x0
  Add the number 4 (0x04) 5 times to W
  What is the expected result?
Pseudo-code / algo:
  [WREG] = 0x0
  [WREG] = [WREG] + 0x04 ---- do this 5 times
  [WREG] = ??

## Slide 13: PIC18F: Exercise – attempt #1
Let’s try using literal instructions:
MOVLW 0x00 [WREG] = ?
ADDLW 0x04 [WREG] = ?
ADDLW 0x04 [WREG] = ?
ADDLW 0x04 [WREG] = ?
ADDLW 0x04 [WREG] = ?
ADDLW 0x04 [WREG] = ?
What’s the result?
Code works(!), but do you (fore-)see any issues?

## Slide 14: PIC18F: Exercise – attempt #2 - BEGIN
Let’s try “looping”
  We need a “counter” – here, a decrementing one
  Initialize WREG to zero
  Initialize the counter to MAX (5 in this case)
  Add 0x04 to WREG
  Decrement the counter
  Check!
    If counter is not zero, keep doing 3, 4 and 5
    Else (if counter is zero), STOP!
Issue:
  Where do we keep the “counter” variable?

## Slide 15: PIC18F: Exercise – attempt #2 - SETUP
Let’s use a RAM File Register (say, 0x30)
  For keeping the “counter” variable
  Could be done thus:
  CNTR EQU 0x30
  MOVLW 0x05 [WREG] = ?
  MOVWF CNTR [CNTR] = 5
  MOVLW 0x0 [WREG] = ?
  Do work (also create a label!)
  WORK ADDLW 0x04 ??
  Now decrement the “counter”
  DECF CNTR, F ??
  Check!
  BNZ WORK ??

## Slide 16: PIC18F: Exercise – attempt #2 – CODE.1
Putting code together, adding directives
  #include “P18F4520.inc”
  CNTR EQU 0x30
  ORG 0x0
  MOVLW 0x05
  MOVWF CNTR
  MOVLW 0x0
  WORK ADDLW 0x04 DECF CNTR, F “loop body”
  BNZ WORK
  END

## Slide 17: PIC18F: Exercise – attempt #2 – CODE.2
Better code - ‘Abstraction’
  #include “P18F4520.inc”
  CNTR EQU 0x30
  COUNT EQU 0x05
  DAT EQU 0x04
  ORG 0x0
  MOVLW COUNT
  MOVWF CNTR
  MOVLW 0x0
  WORK ADDLW DAT
  DECF CNTR, F
  BNZ WORK
  END

## Slide 18: PIC18F: Exercise – attempt #3 – skip
Use skipping!
  #include “P18F4520.inc”
  CNTR EQU 0x30
  COUNT EQU 0x05
  DAT EQU 0x04
  ORG 0x0
  MOVLW COUNT
  MOVWF CNTR
  MOVLW 0x0
  WORK ADDLW DAT
  DECFSZ CNTR, F
  GOTO WORK
  GOTO $
  END

## Slide 19: PIC18F: Debug ‘hooks’
Code development cycle
  Ideate – select algorithm
  Develop – write code
  Debug – remove errors (bugs) found
  Test – test it on ‘test vectors’
  Rinse and repeat!
GOTO $ ‘hook’ – used to stop/halt code-run
  $ stands for currently executing instruction line
  Instn #n
  Instn #n+1
  GOTO $
  Instn #n+2
Remove from production code!

## Slide 20: PIC18F: More loops!
Using an FREG (8-bit)
  Gives us 256 ‘counts’
What if we wanted to count more?
  Use ‘nested’ loops – more than one FREG
Math behind FREG counters
# of FREGS | # of Bits | Loop count
1 | 8 | 256 (28)
2 | 16 | 65536 (216)
3 | 24 | ~16million (224)
4 | 32 | ~4.2billion (232)

## Slide 21: PIC18F: Multi-loop code
2 loops – one inside the other – ‘nested’
Instn #N
Loop1 Instn #L1
Instn #L1+1
Loop2 Instn #L2
Instn #L2+1
DECFSNZ CNT_L2
GOTO Loop2
Instn #L1+2
GOTO Loop1
Instn #N+1

## Slide 22: PIC18F: Exercise learnings!
There are many, many ways to write code
  Almost all will ‘do the job’
For multiple algorithms, evaluate ‘relative cost’:
  Code (space)
  Time (speed)
  Energy (power-draw)
  Modularity (maintenance)
  Re-use (library)
Production code is a cost-optimization problem
  Embedded ‘mantra’: write less code to do more!

## Slide 23: Compare instructions

## Slide 24: PIC18F: Instructions - comparison
CPFSEQ
  Compare FREG (with W) and Skip if Equal
    Skip if [FREG] == [WREG]
CPFSGT
  Compare FREG (with W) and Skip if Greater than
    Skip if [FREG] > [WREG]
CPFSLT
  Compare FREG (with W) and Skip if Less than
    Skip if [FREG] < [WREG]

## Slide 25: PIC18F: Exercise #2: Comparison
Problem statement:
  Increment FREG 0x40 in steps of d’10’ till you reach d’100’
Algorithm:
  Define 2 FREGs, FREG1 and FREG2
  Initialize [FREG1] to d’0’ - will be incremented
  Initialize [FREG2] to d’100’ - will hold the final value
  Implement a loop
    Add d’10’ to [FREG]
    Check [FREG1] and [FREG2] for equality
    Exit the loop if the two become equal
Loop without counter!
  But has a clear exit condition

## Slide 26: PIC18F: Exercise #2 – code
  #include “P18F4520.inc”
  FREG1 EQU 0x40
  FREG2 EQU 0x50
  STEP EQU d’10’
  FINAL EQU d’100’
  ORG 0x0
  CLRF FREG1
  MOVLW FINAL
  MOVWF FREG2 ; [FREG2] = FINAL
  LOOP MOVLW STEP
  ADDWF FREG1, F ; [FREG1] += STEP
  MOVF FREG2, W
  CPFSEQ FREG1 ; Compare [FREG1] & [WREG]
  BRA LOOP
  GOTO $
  END

## Slide 27: Functions

## Slide 28: Programming: Concept of modularity
Divide and Rule
  When faced with a big problem
    Break it down into small manageable pieces / chunks
  In the computing / coding world
    Manifests as modular code
    Functions, sub-routines
Function
  Independent piece of code that does ‘some work’
  Needs to be ‘called’
  After doing the work, it ‘returns’ back to the ‘caller’
  Code re-use:
    Same code can be called any number of times!

## Slide 29: PIC18F: Function – structure
Function body:
FUNC1 ADDLW 0x04
SUBWF 0x30 “function body”
MOVWF 0x45
RETURN
Function call:
Instn #n
CALL FUNC1
Instn #n+1

## Slide 30: PIC18F: Instructions – function calls
CALL
  Call the function with that label
  Example: CALL FUNC1
  4-byte instruction – 20 bits for JUMP-TO address
    Can jump anywhere within the code space
RCALL
  Short call the function with that label
  Example: RCALL FUNC1
  2-byte instruction – 11 bits for JUMP-TO address
    Jump restricted to a range of 2048
RETURN
  Return from the function – back to caller
Tip: RCALL saves code-space when jump is short

## Slide 31: PIC18F: Functions and the stack
Example: View of code memory
Code address Instructions
m1 Instn #n
m2 CALL FUNC1
m3 Instn #n+1
Function call sequence
  The code address after the function call is saved
    m3 is ‘pushed’ to the stack
  FUNC1 ‘runs’
    [PC] = FUNC1’s code address
  When FUNC1 returns, stored address is ‘popped’ from the stack
    [PC] = m3
  Code flow returns to the point after the function call

## Slide 32: PIC18F: LIFO Stack for nested functions
Code with nested functions
Instn #n
CALL FUNC1
Instn #n+1
…
FUNC1 Instn #o
Instn #o+1
CALL FUNC2
Instn #o+2
RETURN
FUNC2 Instn #p
Instn #p+1
RETURN
[PC] sequence: n, o, o+1, p, p+1, o+2, n+1
PC and Stack interactions
[PC] = Addr (#n)
- FUNC1 called, Stack push
[PC] = Addr(#o), SP = Addr(#n+1)
- FUNC1 runs
[PC] = Addr(#o+1)
- FUNC2 called, Stack push
[PC] = Addr(#p), SP = Addr(#o+2)
- FUNC2 runs
[PC] = Addr(#p+1)
- FUNC2 returns, Stack pop, FUNC1 runs
[PC] = Addr(#o+2)
- FUNC1 returns, Stack pop, Back!
[PC] = Addr(n+1)

## Slide 33: Programming: Software delay
Concept of a delay
  A wait for a fixed amount of time
  Used for interacting with devices at different speeds
A function to generate a delay
  Generating delay by writing code – ‘software delay’
  Function body:
    Create a loop (initialize a counter)
    Loop body:
      Idle – do nothing!
      Decrement the counter
      If the counter is not-zero, rinse and repeat!
      Else, exit the loop
    Return from the function

## Slide 34: PIC18F: Functions: Software delay
Main code
CNTR EQU 0x50
DLY_VAR EQU 0x20
ORG 0x0
…
CALL DELAY
…
…
CALL DELAY
…
►Code re-use
►Modularity
Function
ORG 0x300
DELAY MOVLW DLY_VAR
MOVWF CNTR
LOOP NOP
NOP
NOP
DECF CNTR, F
BNZ LOOP
RETURN

## Slide 35: PIC18F: Why not software for delay?
Software delay code is rarely used in production
Issues with software generated delays:
  Poor ability to give ‘strict’, ‘precise’ delays
    If interrupts are enabled, can get interrupted when running delay code
    Once interrupted:
      Has to suspend running the delay code
      On return, resumes running the delay code
  Wasteful way of generating a delay
    NOP also consumes power!
  As code size and complexity grows
    Difficult to tune delay functions for exactness
So what do we use?
  Hardware generated delays – timers, counters

## Slide 36: PIC18F: Return value from functions
Functions can do more than ‘perform work’
  They can take values from the caller
    Called input arguments
  They can also give back values to the caller
    Called return values / output arguments
  Caller - callee interaction : bi-directional
WREG is usually used for these purposes
An example of WREG used for returning values
  Instruction: RETLW
    Return from a function with Data in WREG
    Example: RETLW 0x20
    Effect: [WREG] = 0x20, automatic return

## Slide 37: Programming: Implementing lookups
Implement a function that returns the square of input
  Assume input 0 ≤ x ≤ 9
  Let’s call the function SQR
  Let’s use WREG as input as well as output argument
  Examples:
    For [WREG] = 0x02, CALL SQR should return [WREG] = 0x04
    For [WREG] = 0x03, CALL SQR should return [WREG] = 0x09, …
  Pre-compute answers and store them – ‘lookup table’
  Code structure:
    Main code: Fills WREG with x, calls SQR
    Function code (SQR): Computes and returns x2 in WREG

## Slide 38: PIC18F: Squaring by lookup table
INPUT EQU 0x02
OUT_REG EQU 0x30
ORG 0x0
MOVLW INPUT ; [WREG] = INPUT
CALL SQR
MOVWF OUT_REG ; [OUT_REG] = Answer!
SQR MULLW 0x02 ; [PRODL] = [WREG] x 2
MOVF PRODL, W ; bring it back to WREG
ADDWF PCL, F ; [PCL] += [WREG] + 2
RETLW d’0’
RETLW d’1’
RETLW d’4’
…
RETLW d’81’
► 16-bit (2-byte) instn → [PCL] += 2 by default
► [PCL] += 2 + 2*input
► Strategically place RETLWs to return the square in WREG
input | 2*input
0 | 0
1 | 2
2 | 4

## Slide 39: PIC18F: Journey so far
Algorithmic options
  Good code, not-so-good code
Looping
  NOP
Comparison-induced branching
Functions
  Modularity
  Code re-use
  Scalability – teams of programmers
Function call related
  CALL, RCALL
  RETURN, RETLW

## Slide 40: PIC18F: Instructions – Part 2 Summary
Programming constructs
  Branching
    Unconditional, conditional
  Comparison
  Looping
    Loop entry, exit
  Delay generation using loops
  Functions
    Call, return, nesting
  Lookup tables

## Slide 41: Thank you!