## Slide 1: The PIC microcontroller
PIC18F4520: Instruction Set – Part 3

## Slide 2: PIC18F: Controller Architecture

## Slide 3: PIC18F: Instruction set grouping

## Slide 4: PIC18F: Notational convention
WREG
  W Register
FREG
  File Register (any register location from GPR Bank 0 / SFR)
[X]
  Contents of register X
    [WREG] = 0x02 ↔ WREG’s contents become 0x02
    [0x20] = 0x34 ↔ RAM File Register 0x20 content becomes 0x34
    [X] = [Y] ↔ Contents of Y are copied into X
Number systems
Decimal | d’10’
Hexadecimal | h’4A’ or 0x4A
Binary | b’1000 0010’

## Slide 5: The world of pointers

## Slide 6: Programming: Concept of variables
Programs use ‘variables’ to hold values
  x = 5, y = 10.25
Variables come in many types
  Simple types
    Integers – Hold integer values (+, 0, -)
      int i = 10, j = -100;
    Characters – Hold characters (ASCII)
      char c = ‘a’;
    Floats – Hold floating point (real number) values
      float f = 0.123, g = -1.453
    Strings – Hold several characters ‘together’
      char str[] = ‘hello!’
  Complex types
    arrays, complex numbers
    trees, lists, stacks, heaps, dictionaries, …
Pointers are a special type of variable
  They don’t hold values, but ‘addresses’ of other variables

## Slide 7: Programming: The pointer concept
Let’s take a variable (say, x )
  x = 10
    x has a value, and the value is 10
  x has to exist somewhere in data memory
    x has an address, say 0x20
A pointer (say, p) can hold x’s address for us
  Effectively ‘pointing to x’
  So, p = 0x20
This gives us 2 methods to access / change x
  Directly by saying x = 100
  Indirectly by going through p
d’10’
x
0x20
0x20
p
0xMN

## Slide 8: Addressing modes

## Slide 9: PIC18F: Addressing modes
Immediate addressing
  Using literal instructions
    Number appearing in the instruction is ‘data’
  Example: ADDLW 0x20 ; [WREG] = [WREG] + 0x20
Register direct addressing
  FREG used for computation / movement
    Number appearing in the instruction is ‘FREG location’
  Example: ADDWF 0x20, F ; [FREG] = [FREG] + [WREG]
Register indirect / pointer addressing
  Use pointer register to address FREG
Table addressing
  Moving data from code memory to data memory

## Slide 10: Pointer registers

## Slide 11: PIC18F: Pointer registers
PIC18F has a pointer register framework
Pointer register
  Does not hold a value
  Instead, holds address of another FREG
PIC18F pointer registers are called FSRs
  File Selection Register Not SFR!
  PIC18F has 3 such FSRs
    FSR0, FSR1, FSR2 – 12 bits each
    Each such FSR can ‘point’ to any FREG (0x000 to 0xFFF)
    But not by default!
      We have to make it point to an FREG
      The instruction to do that is LFSR

## Slide 12: PIC18F: Instructions - LFSR
LFSR
  Load an FSR with the address of an FREG
  Syntax: LFSR n, FREG_address where 0 ≤ n ≤ 2
  Example:
  CNT_REG EQU 0x20
  LFSR 0, CNT_REG
  Effect: [FSR0] = CNT_REG’s address = 0x20
  After this point, we can use FSR0 to access CNT_REG
  But how? Not by using FSR0, but another register INDF0
  Example:
  MOVLW 0x10
  MOVWF INDF0
  Effect: [CNT_REG] = [0x20] = 0x10!
  So, FSR points and INDF gives data access

## Slide 13: PIC18F: FSR family
PIC18F has 3 FSRs and correspondingly, 3 INDFs
Care should be taken when using pointers to:
  Load proper FSR before doing data access
    Called pointer initialization
  Using the proper, corresponding INDF for data access
    Called pointer de-referencing
Bad example:
LFSR 0, 0x20
MOVWF INDF2
FSR | INDF
FSR0 | INDF0
FSR1 | INDF1
FSR2 | INDF2

## Slide 14: Programming: Chunk move – Idea
Real-world data moves:
  programs need to move
  chunks of data
  from one location in memory
  to another location in memory
Typical problem statement:
  Move 10 bytes of data from starting location 0x20 to location starting at 0x30
Called memcopy
Most efficiently done using pointer-loop combo
0x20 | 0x21 | … | 0x29
0x01 | 0x02 | … | 0x0A
0x30 | 0x31 | … | 0x39
0x01 | 0x02 | … | 0x0A

## Slide 15: PIC18F: Chunk move – Method
Set up a loop counter variable
Use 2 pointers – one for source, another for destination
  Say, FSR0 for src, FSR1 for dest
Initialize pointers to point to src and dest
  LFSR 0, SRC_REG ; [FSR0] = SRC_REG
  LFSR 1, DST_REG ; [FSR1] = DST_REG
Use a MOVFF to move the underlying data
  MOVFF INDF0, INDF1
    Effect: [DST_REG] = [SRC_REG]
Increment pointers (not SRC_REG, DST_REG)
  INCF FSR0L
  INCF FSR1L
Rinse and repeat this loop using counter variable
Issue: FSRs are 12-bit! ALU is 8-bit!

## Slide 16: PIC18F: Pointer register increments
12-bit FSRs cannot be incremented / decremented in ALU
Handling 12-bit operation – special registers
Complete FSR family
Pointer register | Effect / usage
POSTINC | Get the data, then increment FSR
POSTDEC | Get the data, then decrement FSR
PREINC | Increment FSR, then get the data
FSR0 | FSR1 | FSR2
INDF0 | INDF1 | INDF2
POSTINC0 | POSTINC1 | POSTINC2
POSTDEC0 | POSTDEC1 | POSTDEC2
PREINC0 | PREINC1 | PREINC2

## Slide 17: PIC18F: An insight into POSTINC
Move contents of:
  0x20 to 0x30, and 0x21 to 0x31
Initialize pointer registers
  LFSR 1, 0x20 ; [FSR1] = 0x20
  LFSR 2, 0x30 ; [FSR2] = 0x30
Get 0x20’s contents into W, thence to 0x30
  Not with INDF, but with POSTINC
  MOVF POSTINC1, W ; [WREG] = [0x20], FSR1+=1
  MOVWF POSTINC2 ; [0x30] = [WREG], FSR2+=1
  Now, FSR1 points to 0x21, FSR2 to 0x31
  MOVFF POSTINC1, POSTINC2
  ; [0x31] = [0x21], FSR1+=1, FSR2+=1
  Using a POSTINC gives us a ‘free’ post-increment of the FSR
  Loop this to get smooth movement of large chunks!
2 variants!

## Slide 18: PIC18F: Chunk move problem – solved!
Moving 10 bytes from 0x20 to 0x30 using POSTINC pointers
#include "P18F4520.inc"
SRC_REG EQU 0x20
DST_REG EQU 0x30
CNT_REG EQU 0x10
COUNT EQU d'10'
ORG 0x0
MOVLW COUNT
MOVWF CNT_REG
LFSR 1, SRC_REG
LFSR 2, DST_REG
LOOP MOVFF POSTINC1, POSTINC2
DECFSZ CNT_REG, F
BRA LOOP
GOTO $
END

## Slide 19: Table addressing

## Slide 20: Computing: Remembering data!
PIC18F has 2 memories
  Non-volatile Code Memory
  Volatile Data Memory
By default
  Code/program/instructions go into Code Memory
  Data goes into Data Memory
But what if we want to remember some data?
  Keep this data in code memory!
But how does my code access this data?
  All instructions learnt so far deal only with data memory

## Slide 21: PIC18F: Putting data into code memory
Special directives to put data into code memory
  DB (Define Byte)
  Examples:
  ORG 0x400
  VAL1 DB 0x20 ; hexadecimal
  VAL2 DB h’30’ ; hexadecimal
  VAL3 DB d’25’ ; decimal
  VAL4 DB b’10000010’ ; binary
  VAL5 DB ‘a’ ; character
  VAL6 DB “Hello!”, 0 ; string, null-terminated
That’s fine, but which location in code memory?
Should never be ORG 0x0!

## Slide 22: PIC18F: Mixing Code & Data
Putting code and data into code memory
#include “P18F4520.inc”
REG1 EQU 0x20
ORG 0x0
MOVLW 0x00
MOVWF REG1
ORG 0x400
DAT1 DB d’201’
STR1 DB “Hello!”, 0
END
Ensure that they don’t mix / overlap!
Code
Data
non-volatile!

## Slide 23: PIC18F: Getting data from code memory
Data in code memory cannot be acted upon!
  To use it, we need it back in data memory
Dedicated set of instructions and 2 SFRs
  For getting (non-volatile) data
  from code memory
  back into data memory
Table processing framework
  SFRs:
    TABLAT (8-bit), TBLPTR (21-bit)
  Instructions:
    TBLRD*, TBLRD*+, TBLRD+*, etc.

## Slide 24: PIC18F: Table processing – SFRs
TABLAT – Table Latch
  8-bit register
  Intermediary for data move from Code memory to Data memory
    Receives the data byte on a Table Read
    From here, move it to WREG or any other FREG
TBLPTR – Table Pointer Register
  21-bit register – cannot be initialized in 1 instruction
  Split into 3 parts:
    TBLPTRL (low - 8-bits)
    TBLPTRH (high - 8-bits)
    TBLPTRU (upper - 5-bits)
5-bits
TBLPTRU
8-bits
8-bits
TBLPTRH
TBLPTRL
21 bits

## Slide 25: PIC18F: Instructions – Table processing
TBLRD*
  Read 1 data byte
    From code address pointed to by TBLPTR
    Into TABLAT
TBLRD*+
  Read 1 data byte
    From code address pointed to by TBLPTR
    Into TABLAT
  Increment TBLPTR – post-increment
TBLRD+*
  Increment TBLPTR – pre-increment
  Read 1 data byte
    From code address pointed to by TBLPTR
    Into TABLAT

## Slide 26: PIC18F: Table processing example
Put 1 byte in code memory (0x500), read it in FREG (0x20)
#include “P18F4520.inc”
FREG1 EQU 0x20
ORG 0x0
MOVLW 00
MOVWF TBLPTRU
MOVWF TBLPTRL
MOVLW 0x05
MOVWF TBLPTRH ; TBLPTR = 0x000500
TBLRD* ; read from TBLPTR to TABLAT
MOVFF TABLAT, FREG1
GOTO $
ORG 0x500
DAT DB ‘B’
END

## Slide 27: PIC18F: Table Read Flow
MOVLW 0x05
MOVWF TBLPTRH
TBLRD*
MOVFF TABLAT, FREG1
--
--
‘B’
Code memory
0x006
0x500
--
‘B’
Data memory
FREG1
WREG
TBLPTRU
TABLAT
TBLPTRH
TBLPTRL
0x00
0x00
0x05
0x00
‘B’
MOVWF TBLPTRL
MOVWF TBLPTRU
MOVLW 0x0
0x008
0x00A
0x00C
0x004
0x002
0x000
0x05
Non-volatile
Volatile
●
●
●
●
●
●
●

## Slide 28: PIC18F: Advanced table processing
Read a null-terminated string from code memory (0x400) into data memory (starting at 0x30)
#include “P18F4520.inc”
DST EQU 0x30
ORG 0x0
MOVLW 00
MOVWF TBLPTRU
MOVWF TBLPTRL
MOVLW 0x04
MOVWF TBLPTRH ; SRC
LFSR 1, 0x30 ; DST
LOOP TBLRD*+ ; read from TBLPTR, post-increment TBLPTR
MOVF TABLAT, W
BZ EXIT
MOVWF POSTINC1 ; move to FSR1, post-increment FSR1
BRA LOOP
EXIT GOTO $
ORG 0x400
DAT DB “Hello world!”, 0
END

## Slide 29: PIC18F: String move learnings
Pointered access to code memory
  TBLPTR
Pointered access to data memory
  FSR1
Pointer-loop combination to move data chunk
Multi-step movement
  Code memory → TABLAT → WREG → FREG
Loop without counter
  But with an exit condition!
Use of Z Flag to exit the loop

## Slide 30: PIC18F: Instructions – Table write
PIC has Table Write instructions as well
  TBLWT*
  TBLWT*+
  TBLWT+*
  TBLWT*-
Not implemented so well in MPLAB Simulator
Leads to code changing contents of code memory
  Vicious loop – best avoided!

## Slide 31: Modules

## Slide 32: PIC18F: Projects with multiple asm files
So far, we dealt with single asm file MPLABX projects
  What if project requirements and code spill beyond 1 asm file?
MPLABX ‘modules’
  Create a single ‘exe’ from multiple asm files
  Each such asm file is called a ‘module’
Interaction between ‘modules’
  Takes place via ‘GLOBAL’ and ‘EXTERN’ declarations
  GLOBAL
    Declares that this module and its contents are ‘global’
    Available for all other modules to use
  EXTERN
    A module that wants to use GLOBALS declares them as EXTERN
    Short for ‘external’ – coming from somewhere else

## Slide 33: PIC18F: Module example
Main.asm
#include “P18F4520.inc”
OUT EQU 0x20
EXTERN COMPUTE
ORG 0x0
MOVLW 0x10
CALL COMPUTE
MOVWF OUT
BRA $
END
Compute.asm
#include “P18F4520.inc”
GLOBAL COMPUTE
PGM CODE
COMPUTE MULLW 0x02
MOVF PRODL, W
RETURN
END

## Slide 34: PIC18F: Module with code placement
Main.asm
#include “P18F4520.inc”
OUT EQU 0x20
EXTERN COMPUTE
ORG 0x0
MOVLW 0x10
CALL COMPUTE
MOVWF OUT
BRA $
END
Compute.asm
#include “P18F4520.inc”
GLOBAL COMPUTE
COMPUTE CODE 0x100
COMPUTE MULLW 0x02
MOVF PRODL, W
RETURN
END

## Slide 35: PIC18F: Module compile flow
Assembler:
  Main.asm
    Assembled to main.o
  Compute.asm
    Assembled to compute.o
Librarian
  N/A
Linker
  Links main.o and compute.o
    Code placement, variable (symbol) resolution, memory handling
  To create single exe (production.hex)

## Slide 36: PIC18F: Instructions – Part 3 Summary
Programming constructs
  Pointers and indirect addressing
  Data chunk movement - memcopy
PIC18F
  Addressing modes
  Pointer register framework
  Table processing framework
  Code memory – data memory interactions
    Data placement in code memory
    Data movement from code memory to data memory
      1-byte
      Chunk (string)
Project constructs
  Modules
  Multi-asm file projects

## Slide 37: Thank you!