## Slide 1: The PIC microcontroller
PIC18F4520: IO Port Programming

## Slide 2: PIC18F: Controller Architecture

## Slide 3: PIC18F: Notational convention
WREG
  W Register
FREG
  File Register (any register location from GPR Bank 0 / SFR)
[X]
  Contents of register X
    [WREG] = 0x02 ↔ WREG’s contents become 0x02
    [0x20] = 0x34 ↔ RAM File Register 0x20 content becomes 0x34
    [X] = [Y] ↔ Contents of Y are copied into X
Number systems
Decimal | d’10’
Hexadecimal | h’4A’ or 0x4A
Binary | b’1000 0010’

## Slide 4: Digital i/o ports

## Slide 5: Electronics: Concept of I/O Ports
Interfacing with the real world
  Digital devices – using digital I/O ports
    1/2/3-pin devices – using I/O port pins
    Serial devices – using I/O port pins or serial ports
    Parallel devices – using I/O port pins in parallel
  Analog devices – using analog input channels and ADCs
Digital devices
  Talk ‘digital’ – the language of 1’s and 0’s
    Voltages:
      Logic high (1): 5V, 3.3V, 1.8V, …
      Logic low (0): 0V

## Slide 6: PIC18F family: I/O port wise

## Slide 7: PIC18F: I/O ports
PIC18F4520 has 5 Digital Bidirectional I/O ports
  Port function multiplexed with other functions
  Labelled alphabetically
    PORTA, PORTB, PORTC, PORTD (8-bits each)
    PORTE (4-bits)
  Pin-out wise, the pins are named RXn
I/O Port | Port pin(s)
PORTA | RA0 – RA7
PORTB | RB0 – RB7
PORTC | RC0 – RC7
PORTD | RD0 – RD7
PORTE | RE0 – RE3

## Slide 8: PIC18F4520: I/O ports in the pin-out

## Slide 9: PIC18F: I/O port usage
Being a soft-configured controller
  Port pin functionality needs to be coded
  Port pin direction also needs to be coded
Each PORT has 3 port registers for interaction and control
  TRIS (tristate) register
    Controls port/pin direction
    On a per-pin basis, 1 makes it input, 0 makes it output
  PORT register
    Exchange of data with device connected to the port
  LAT (latch) register
    Used for read-modify-write operations – not used in this course

## Slide 10: PIC18F4520: PORT A details
PORT A
  Port size (width)
    8 bits
  Pins
    RA0 – RA7
  Registers (reside in the SFR!)
    Direction
      TRISA – 8-bit
    Data
      PORTA – 8-bit
    Latch
      LATA – 8-bit
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0
PORTA
TRISA
data
direction

## Slide 11: PIC18F: Using I/O PORT B
Schematic lookup
  Peruse schematic and confirm connections involving PORTB
  Determine data flow direction (input / output)
Algorithmic decision
  Determine how you will use PORTB for interaction
  Incorporate timing considerations, if any
Coding
  Set up pin / port direction(s) by writing value(s) to TRISB
  Perform data transfer(s) by reading/writing to PORTB

## Slide 12: PIC18F: PORTB as an output port
Consider this code MOVLW b’00000000’
MOVWF TRISB
LOOP MOVLW 0x55
MOVWF PORTB
CALL DELAY
MOVLW 0xAA
MOVWF PORTB
CALL DELAY
BRA LOOP
‘User’ view of the PIC
PIC18F4520
PORTB
Called ‘port-wise’ usage of PORTB
WREG
What does this code do?

## Slide 13: PIC18F: PORTB pin(s) as output
Consider this code
BCF TRISB, 0
LOOP BSF PORTB, 0
CALL DELAY
BCF PORTB, 0
CALL DELAY
BRA LOOP
‘User’ view of the PIC
PIC18F4520
RB0
Called ‘pin-wise’ usage of PORTB

## Slide 14: PIC18F: PORTB as an input port
Consider this code
INREG EQU 0x20
MOVLW b’11111111’
MOVWF TRISB
MOVF PORTB, W
MOVWF INREG
‘User’ view of the PIC
PIC18F4520
PORTB
Called ‘port-wise’ usage of PORTB
DEVICE
WREG
INREG

## Slide 15: PIC18F: PORTB pin(s) as input
RB2
Consider this code
BSF TRISB, 2
LOOP BTFSS PORTB, 2
BRA LOOP
…
‘User’ view of the PIC
Called ‘pin-wise’ usage of PORTB
PIC18F4520
1-pin DEVICE
Algo

## Slide 16: Real-world scenarios

## Slide 17: Scenario #1: Implement festive lights!
Problem statement
  Assume 8 LEDs are attached to all 8 pins of PORTB
  Create a pattern where each LED lights up after a delay
Think!
  PORTB access method: port-wise / pin-wise
  PORTB direction: input / output

## Slide 18: Scenario #1: Circuit schematic
LED working principle
LEDs in our scenario
PIC18F4520
PORTB
For LED to ‘light up’, the anode needs to have a high positive voltage (> Vf )
…

## Slide 19: Scenario #1: Code
CLRF TRISB ; Make all pins output
BSF PORTB, 0 ; RA0 LED
CALL DELAY
BSF PORTB, 1 ; RA1 LED
CALL DELAY
…
BSF PORTB, 7 ; RA7 LED

## Slide 20: Scenario #1: Twist!
What would happen:
  If we used a ‘port-wise’ access method for PORTB?
  CLRF TRISB ; Make all pins output
  MOVLW 0xFF ; Fill with all ones
  MOVWF PORTB ; Push to PORTB
Which problem statement does this code solve?

## Slide 21: Scenario #2: Making waves!
Problem statement
  Create a ‘regular’ square wave on pin RC0 of PORTC
Think!
  ‘Regular’ square wave → duty cycle is 50%
    Equal tON and tOFF times → tON = tOFF
  We could use a BTG (bit toggle) instruction!
T
f = 1 / T
Square wave properties
T = Period = tON + tOFF
f = Frequency
tON
tOFF

## Slide 22: Scenario #2: Code for square wave
BCF TRISC, 0 ; Make this pin output
LOOP BTG PORTC, 0 ; Toggle away
CALL DELAY ; Delay for some time
BRA LOOP ; Repeat
How would the code change if we used BSF, BCF?

## Slide 23: Scenario #3: Making uneven waves!
Problem statement
  Create a square wave of DC 66% on pin RD3
Think!
  DC 66% → 66% ON, rest of the time (~33%) OFF
    66:33 → 2:1 → tON = 2 * tOFF
  Can we use a BTG (bit toggle) instruction here?
T
f = 1 / T
PWM Square wave properties
T = Period = tON + tOFF = 3 * tOFF
f = Frequency
tON
tOFF

## Slide 24: Scenario #3: Code for 66% DC
BCF TRISD, 3 ; make this pin output
LOOP BSF PORTD, 3 ; ON
CALL DELAY ; for
CALL DELAY ; 2 times!
BCF PORTD, 3 ; OFF
CALL DELAY ; for
BRA LOOP ; (only) 1 time!
How does this code change if DC needed is 33%?
How about DC of 15%?!

## Slide 25: Scenario #4: Multiple devices
Problem statement
  Keep monitoring a 1-pin device connected to RB4
  if
    it goes HIGH
  then
    send a byte 0x45 to an (8-pin) device connected to PORTC
    send a HIGH-to-LOW pulse to a 1-pin device connected to RA2
Think!
  Ports?
  Access methods for each such port?
  Port directions?

## Slide 26: Scenario #4: Circuit schematic
Input as well as output devices!
PIC18F4520
PORTC
RB4
1-pin DEVICE
DEVICE
1-pin DEVICE
RA2
Algo
0x45
if
then

## Slide 27: Scenario #4: Code
BSF TRISB, 4 ; input – pin-wise
CLRF TRISC ; output – port-wise
BCF TRISA, 2 ; output – pin-wise
MOVLW 0x45 ; data pre-load
LOOP BTFSS PORTB, 4 ; check!
BRA LOOP
MOVWF PORTC ; move byte
BSF PORTA, 2 ; HIGH
BCF PORTA, 2 ; then LOW

## Slide 28: PIC18F: I/O Ports Summary
What are I/O Ports
PIC18F
  Nature of I/O ports
  TRIS, PORT and LAT registers
  Access methods: ‘port-wise’, ‘pin-wise’
  Port directions
Square wave generation
  Changing DC and deriving PWM
    Simple ratios
Interfacing multiple devices
  Code for handling if-then-else loops

## Slide 29: Thank you!