## Slide 1: The PIC microcontroller
PIC18F4520: Configuration Bits

## Slide 2: PIC18F: Controller Architecture

## Slide 3: PIC18F: Notational convention
WREG
  W Register
FREG
  File Register (any register location from GPR Bank 0 / SFR)
[X]
  Contents of register X
    [WREG] = 0x02 ↔ WREG’s contents become 0x02
    [0x20] = 0x34 ↔ RAM File Register 0x20 content becomes 0x34
    [X] = [Y] ↔ Contents of Y are copied into X
Number systems
Decimal | d’10’
Hexadecimal | h’4A’ or 0x4A
Binary | b’1000 0010’

## Slide 4: pic18F Config bits

## Slide 5: PIC18F: Configuration Bits
Configuration Bits
  Control the PIC’s behavior
  Enable / Disable various hardware features of the PIC
  Available through Config Registers
    Addresses 0x300001 through 0x30000D
  Significant ones:
    CONFIG1H (0x300001): Frequency / Oscillator Selection
    CONFIG2L (0x300002): PWRT and BOR Control
    CONFIG2H (0x300003): WDT Control

## Slide 6: PIC18F4520: CONFIG1H
  IESO: Internal/external oscillator switchover bit
  FCMEN: Failsafe clock monitor enable bit
  FOSC3:0 <4 bits>
    0000: LP
    0001: XT
    0010: HS
    0011: External RC, CLK0 on RA6
    0100: External clock, CLK0 on RA6
    0101: External clock, RA6 as port pin
    0110: HS, PLL enabled
    0111: External RC, RA6 as port pin
    1000: Internal oscillator block, RA6, RA7 as port pins
    1001: Internal oscillator block, CLK0 on RA6, RA7 as port pin
    101x, 11xx: External RC, CLK0 on RA6
IESO
FCMEN
-
-
FOSC3
FOSC2
FOSC1
FOSC0
PIC18F4520
fOSC
fOSC/4
RA6
RA7

## Slide 7: PIC18F4520: OSC1/CLKI/RA7, OSC2/CLKO/RA6

## Slide 8: Clock config and system design

## Slide 9: PIC18F4520: Clock circuits (LP, XT, HS)
Circuit schematic(s)
Clock modes
FOSC<3:0>
0000: LP
  Low-power crystal
0001: XT
  Crystal / resonator
0010: HS
  High-speed crystal

## Slide 10: PIC18F4520: Clock circuits (EC, ECIO)
Circuit schematic(s)
Clock modes
FOSC<3:0>
0100: EC
(external clock, CLK0 on RA6)
0101: ECIO
(external clock, IO on RA6)

## Slide 11: PIC18F4520: Clock circuits (RC, RCIO)
Circuit schematic(s)
Clock modes
FOSC<3:0>
0011, 101x, 11xx: RC
(external RC, CLK0 on RA6)
0111: RCIO
(external RC, IO on RA6)

## Slide 12: PIC18F4520: Clock circuits (HS-PLL)
Circuit schematic
Clock mode
FOSC<3:0>
0110: HS-PLL
(High-speed crystal, PLL enabled)

## Slide 13: PIC18F4520: Internal Clock Block
FOSC<3:0>: 1000, 1001: Internal Clock

## Slide 14: PIC18F4520: CONFIG2L
  BORV<1:0>: Brown-out reset voltage bits
    11: Minimum setting (2.00V min)
    10: 2.65V min
    01: 4.11V min
    00: Maximum setting (4.36V min)
  BOREN<1:0>: Brown-out reset enable bits
    00: BOR disabled in hardware as well as software
    01: BOR enabled, controlled in software (runtime enable/disable)
    10: BOR enabled in hardware, disabled in sleep mode
    11: BOR enabled in hardware only
  PWRTEN: Power-up timer enable bit
    1: PWRT enabled, 0: disabled
-
-
-
BORV1
BORV0
BOREN1
BOREN0
PWRTEN
LP (low power)

## Slide 15: PIC18F4520: CONFIG2H
  WDTPS<3:0>: Watchdog timer post-scale select bits
    0000 → 1:1
    0001 → 1:2
    0010 → 1:4
    …
    1110 → 1:16384
    1111 → 1:32768
  WDTEN: Watchdog timer enable bit
    1: WDT enabled, 0: WDT disabled
-
-
-
WDTPS3
WDTPS2
WDTPS1
WDTPS0
WDTEN
Watchdog Timer info:
Driven by internal oscillator
Nominal ~4msecs, can be post-scaled to ~131secs

## Slide 16: PIC18F4520: Config Bits control in IDE
Configuration Bits window in MPLABX IDE

## Slide 17: PIC18F4520: Config bits summary
Configuration Bits
  Control the behavior of the PIC
  Enable / disable various hardware features
  Available as a user-friendly, editable table in MPLABX IDE
    Automatic code generation (for inserting into project)
For more details, link to the Controller Datasheet
  http://ww1.microchip.com/downloads/en/DeviceDoc/39631E.pdf

## Slide 18: Thank you!