## Slide 1: The PIC microcontroller
PIC18F4520: Timers and Counters

## Slide 2: PIC18F: Controller Architecture

## Slide 3: PIC18F: Notational convention
WREG
  W Register
FREG
  File Register (any register location from GPR Bank 0 / SFR)
[X]
  Contents of register X
    [WREG] = 0x02 ↔ WREG’s contents become 0x02
    [0x20] = 0x34 ↔ RAM File Register 0x20 content becomes 0x34
    [X] = [Y] ↔ Contents of Y are copied into X
Number systems
Decimal | d’10’
Hexadecimal | h’4A’ or 0x4A
Binary | b’1000 0010’

## Slide 4: timers

## Slide 5: Electronics: Need for ‘time’
Computing world runs on ‘time’
  Synchronization
  Clocks
  Triggers
  Setup / hold times to talk to sensors / devices
Need for highly accurate sense of time
  Precise, reproducible
  Independent - hardware-module driven
  Resilient
Controllers have timers for this purpose

## Slide 6: Electronics: Concept of a ‘Timer’
Independent clock-driven hardware
Software (code)
  Configuration
  Control: Start, stop
Keeps ‘ticking’; ‘overflow’ event tied to time interval
Timer Components
  Configuration registers
  Timer registers
    Keep count, accumulate ‘ticks’
    8-bit, 16-bit, …
  Clock
    Control speed of ticking

## Slide 7: Electronics: Timer working principle
Let’s consider an 8-bit timer
  Timer register is initialized
    Often, to 0x00
  Timer is ‘started’
  Starts ‘ticking’, every tick increments timer register
  Timer register reaches maximum (0xFF)
    Called ‘overflow’ – event is used to derive time
  Timer register gets reset to 0x00
  Timer starts ‘ticking’ and counting again
For 16-bit timer
  Timer register initialized to 0x0000
  Overflows when timer register reaches 0xFFFF
0x00
0xFF
8-bit
0x0000
0xFFFF
16-bit

## Slide 8: PIC18F: Timer details
PIC18F4520 has 4 Timers
  Timer0, Timer1, Timer2, Timer3
  8-bit / 16-bit / both!
  Dual role – as timer or as counter
Study of Timer0 (other timers are ‘similar’)
  8-bit / 16-bit – Configurable in software
  Registers
    Configuration, status and control – T0CON
    Timer register – TMR0H:TMR0L
  Usable as a counter (T0CLKI)

## Slide 9: PIC18F: TIMER0 Configuration: T0CON
TMR0ON: Timer0 on/off control bit
  1: On, 0: Off
T08BIT: Timer0 8-bit/16-bit mode control
  1: 8-bit, 0: 16-bit
T0CS: Timer0 clock source select
  1: Transition on T0CKI, 0: Use internal clock CLK0
T0SE: Timer0 edge select
  1: High-to-low, 0: Low-to-high
PSA: Timer0 pre-scaler enable
  1: Disable, 0: Enable
T0PS<2:0>: Timer0 pre-scaler ratio select bits
  000: 1:2
  001: 1:4
  010: 1:8
  011: 1:16
  …
  111: 1:256
TMR0ON
T08BIT
T0CS
T0SE
PSA
T0PS2
T0PS1
T0PS0

## Slide 10: PIC18F: Timer0 Resources
Timer registers – depending on 8-bit / 16-bit
  TMR0H:TMR0L
Configuration and control register
  T0CON
Overflow indicator flag
  TMR0IF (part of INTCON register)
    TMR0’s Interrupt Flag
    Goes from 0 to 1 on an overflow event
    Should be reset to 0 before using Timer0, and after an overflow!
  TMR0IE (part of INTCON register)
    If 1, enables TMR0 interrupts
    TMR0 interrupt will be generated on an overflow event
0x00
0xFF
8-bit
0x00
TMR0IF
0x01

## Slide 11: PIC18F: Timer0 – usage method
Initialization / configuration
  Fill T0CON and configure the timer (but don’t start it yet!)
  Fill proper values in TMR0, TMRL
  Reset TMR0IF to 0
Start Timer0 by setting TMR0ON to 1 (T0CON)
Check for TMR0 overflow
  Option #1
    Monitor TMR0IF (INTCON) changing to 1, continuously
    Called ‘polling’ method
  Option #2
    Enable TMR0’s interrupt (set TMR0IE to 1)
    Handle TMR0’s interrupt in an ISR
Stop the timer once you are done using it!

## Slide 12: PIC18F: Timer0 – Real-world problem
Generate a 2 kHz square-wave on RB4 for 10MHz crystal clock
  Main code:
    Make RB4 an output pin
    Configure Timer0 (fill in T0CON)
      16-bit mode, Internal clock source, ratio 1:1 (PSA disabled)
    Clear TMR0IF
    Timer_Loop
      Fill TMR0:TMR0L with a proper value (say T0VAL)
      Call TMR_DLY function
      Toggle RB4
  TMR_DLY function
    Start Timer0 (TMR0ON)
    Monitor TMR0IF going to 1
    Once it goes 1
      Stop Timer0
      Clear TMR0IF
    Return
T
tON
tOFF

## Slide 13: PIC18F: Timer0 – Calculations
TMR_DLY has to generate a delay of
Inputs:
Compute
Recursive thumb rule

## Slide 14: PIC18F: Timer0 – Code
Main code
T0VAL_L EQU 0x8F
T0VAL_H EQU 0xFD
BCF TRISB, 4
MOVLW 0x08 ; b’00001000’
MOVWF T0CON
LOOP1 MOVLW T0VAL_L
MOVWF TMR0L
MOVLW T0VAL_H
MOVWF TMR0H
BCF INTCON, TMR0IF
CALL TMR_DLY
BTG PORTB, 4
BRA LOOP1
TMR_DLY
TMR_DLY BSF T0CON, TMR0ON
LOOP2 BTFSS INTCON, TMR0IF
BRA LOOP2
BCF T0CON, TMR0ON
BCF INTCON, TMR0IF
RETURN
TMR0ON
T08BIT
T0CS
T0SE
PSA
T0PS2
T0PS1
T0PS0

## Slide 15: counters

## Slide 16: PIC18F: Timer0 in counter mode
T0CS: Timer0 clock source select
  1: Transition on T0CKI, 0: Use internal clock CLK0
Steps:
  Put T0CS to 1, reset TMR0H:TMR0L to 0!
  Start Timer0
  Accept external clock / event input from T0CKI pin
  On every ‘event’, TMR0H:TMR0L increment
TMR0ON
T08BIT
T0CS
T0SE
PSA
T0PS2
T0PS1
T0PS0

## Slide 17: PIC18F: Input for Timer0 as counter
External clock here

## Slide 18: PIC18F: Timers, Counters Summary
Concept of timers, counters
Advantages of timer / counter module
  Hardware-driven
  CPU independent
    Leaves CPU free to do something else
      Specially if timer interrupts are enabled
      CPU can now do multi-tasking!
  More accurate and resilient
  Can generate interrupts
    No need to actively poll / monitor
PIC18F timers
  Timer0 as a timer or counter

## Slide 19: Thank you!