## Slide 1: The PIC microcontroller
PIC18F4520: Interrupts

## Slide 2: PIC18F: Controller Architecture

## Slide 3: PIC18F: Notational convention
WREG
  W Register
FREG
  File Register (any register location from GPR Bank 0 / SFR)
[X]
  Contents of register X
    [WREG] = 0x02 ↔ WREG’s contents become 0x02
    [0x20] = 0x34 ↔ RAM File Register 0x20 content becomes 0x34
    [X] = [Y] ↔ Contents of Y are copied into X
Number systems
Decimal | d’10’
Hexadecimal | h’4A’ or 0x4A
Binary | b’1000 0010’

## Slide 4: interrupts

## Slide 5: Programming: Concept of ‘interrupt’
Controller interaction with devices
  Internal devices
    (Multiple) Timers, Counters, ADCs, CCP modules
  External devices
Modes of interaction
  Servicing
    Keyboard, mouse, joystick
  Controlling
    LEDs, 7-segment LEDs, LCDs, Monitors, Displays, Motors
  Collecting data
    Sensors, Accelerometers, Gyroscopes, Cameras, USB devices
  Monitoring
As device interaction increases
  Polling through sequential code becomes onerous
Make the device that needs service ‘interrupt’ the CPU
  Send a special signal to get CPU attention
CPU free to do ‘other’ work - freedom from continuous polling

## Slide 6: PIC18F: Interrupts and types
PIC18F has many types of interrupts
  Internal module originated
    Timer interrupts
    USART/UART interrupts
    PORTB Change interrupts
    ADC interrupts
    CCP generated interrupts
    SSP (synchronous serial port) interrupts
  External (hardware triggered)
    Pin based
General interrupt mechanism
  IE (interrupt enable) bit in some register
    If 1, interrupt is enabled
  IF (interrupt flag) bit in some register
    Goes from 0 to 1 when the ‘interrupt’ comes in

## Slide 7: PIC18F: Interrupt – Controls
On boot, PIC18F has all interrupts disabled
2 levels of interrupt control
  Global level
    GIE bit of INTCON register (actually, GIEH bit)
    If this bit is zero, all interrupts are disabled
  Device/type level
    IE flag controlled
    Example: Timer0 interrupt is enabled if TMR0IE is 1
Illustration: Bit mapping for timer interrupts
.
.
Timer | Enable bit (Register) | Flag bit (Register)
TMR0 | TMR0IE (INTCON) | TMR0IF (INTCON)
TMR1 | TMR1IE (PIR1) | TMR1IF (PIE1)
TMR2 | TMR2IE (PIR1) | TMR2IF (PIE1)
TMR3 | TMR3IE (PIR3) | TMR3IF (PIE2)

## Slide 8: PIC18F: Interrupt – Framework
Interrupt vectors - fixed
  By default, all interrupts are ‘high priority’
  Usually hold hard-jumps; actual handling code will lie elsewhere
  ISR (Interrupt Service Routine)
    Interrupt handler code
    Function – automatically called, and returns differently
What happens on an interrupt?
  If interrupt’s IE bit is 1, and if the interrupt occurs
    GIE is disabled, CPU jumps to the interrupt vector location
    Hard jump at this location will call the ISR
    ISR returns with RETFIE ⇒ enables GIE, then RETURNS
Reset vector | 0x0000
High priority interrupt vector | 0x0008
Low priority interrupt vector | 0x0018

## Slide 9: PIC18F: Interrupt – Code flow
On power-up
  Start from 0x0000
  Hard-jump to START
Booting
  Run START
On interrupt
  GIE→0
  Auto-jump to 0x0008
  Hard-jump to ISR
  Run ISR
  RETFIE (GIE→1, RETURN)
Return to START
  Resume running
GOTO ISR
START …
--
ISR …
--
Code memory
0x006
--
GOTO START
0x008
…
0x200
0x004
0x002
0x000
Reset
Hi-prio
0x202
…
RETFIE
--
…
--
…

## Slide 10: PIC18F: Interrupt – Simulation!
#include "P18F4520.inc"
CNT EQU d'10'
FREG EQU 0x10
ORG 0x0
GOTO START
ORG 0x08
ISR BCF INTCON, TMR0IF ; clear the IF flag!
RETFIE
ORG 0x200
START BSF INTCON, GIE ; enable global interrupts
BSF INTCON, TMR0IE ; enable TMR0 interrupts
MOVLW CNT
MOVWF FREG
L1 NOP
NOP
DECF FREG, F
BNZ L1
GOTO $
END
In INTCON: control TMR0IF, keep watch on GIE, TMR0IF!

## Slide 11: PIC18F: Interrupt – Nesting
When an (enabled) interrupt occurs
  It disables (other) interrupts globally [GIE→0]
  And then jumps to its ISR to service/handle it
But what if another device interrupts the PIC now?!
Concept of ‘nested’ interrupts
  Interrupts that interrupt an interrupt being serviced
By design, PIC can not handle nested interrupts

## Slide 12: PIC18F: Nested Interrupts – Scenario
Assume a system using TMR0 and ADC
  Instead of CPU polling, let them interrupt for service
  Steps for handling the 2 devices:
    Each interface needs its own ISR
      TMR0_ISR, ADC_ISR
    Interrupt flags need to be reset!
  BCF INTCON, TMR0IF
  BCF PIR1, ADIF
    Interrupts need to be enabled
  BSF INTCON, TMR0IE
  BSF PIE1, ADIE
But we have only one vector location (0x0008)
  So how do you place both ISRs?
  Also, what if TMR0 interrupts…
    When ADC_ISR is running?

## Slide 13: PIC18F: Nested Interrupts – Template
Vector code
ORG 0x0008
GOTO ISR_MAPPER
ISR Mapper code
ORG 0x0040
ISR_MAPPER BTFSC INTCON, TMR0IF
GOTO TMR0_ISR
BTFSC PIR1, ADIF
GOTO ADC_ISR
RETFIE
ISR code
ORG 0x200 ORG 0x300
TMR0_ISR … ADC_ISR …
BCF INTCON, TMR0IF BCF PIR1, ADIF
GOTO ISR_MAPPER GOTO ISR_MAPPER
Extensible to multiple number of devices
Cycle through all devices
Return only when all are serviced

## Slide 14: PIC18F: Nested Interrupts – Flowchart
START = Got an interrupt!
Auto-jump to 0x0008
ISR mapper
Is it TMR0?
Jump to TMR0 ISR
Clear TMR0IF
Is it ADC?
Jump to ADC ISR
Clear ADIF
RETFIE
STOP!
Yes
No
No
Yes

## Slide 15: PIC18F: External Interrupts
PIC can be interrupted by ‘external’ devices as well
  Called ‘external’ / ‘hardware’ interrupts
  ISRs need to be in place!
External interrupt details
  Pins (multiplexed w/PORTB)
    INT0 (RB0), INT1 (RB1), INT2 (RB2)
  Enabled via
    INTxIE bits
  Edge triggered (via INTEDGx bits)
    If INTEDGx is 1, it is positive edge; else negative
  Interrupt flags
    INTxIF bits
Bit mapping
.
.
.
.
.
.
Pin | Enable bit (Register) | Flag bit (Register)
INT0 | INT0IE (INTCON) | INT0IF (INTCON)
INT1 | INT1IE (INTCON3) | INT1IF (INTCON3)
INT2 | INT12E (INTCON3) | INT2IF (INTCON3)

## Slide 16: PIC18F: Interrupts Summary
Concept of interrupts
Advantages, pitfalls!
PIC18F
  Interrupt mechanisms
  Interrupt sources
    Internal
    External
  An interesting interrupt simulation!
  Nested interrupts
    Multi-interrupt templates

## Slide 17: Thank you!