## Slide 1: The PIC microcontroller
PIC18F4520: ADC

## Slide 2: PIC18F: Controller Architecture

## Slide 3: PIC18F: Notational convention
WREG
  W Register
FREG
  File Register (any register location from GPR Bank 0 / SFR)
[X]
  Contents of register X
    [WREG] = 0x02 ↔ WREG’s contents become 0x02
    [0x20] = 0x34 ↔ RAM File Register 0x20 content becomes 0x34
    [X] = [Y] ↔ Contents of Y are copied into X
Number systems
Decimal | d’10’
Hexadecimal | h’4A’ or 0x4A
Binary | b’1000 0010’

## Slide 4: ADC from Analog to digital

## Slide 5: Electronics: Concept of ADC
The real-world is analog; the computer world is digital
The two interact only if analog is converted to digital
  Or vice versa!
ADC
  Analog to Digital Converter
Analog voltage
n-bit Digital output
n: resolution of the ADC
VREF : reference voltage
Reference voltage

## Slide 6: Electronics: The ADC process
Consider a 5-bit ADC
ADC is a lossy process
Sampling errors, quantization errors

## Slide 7: Electronics: ADC Glossary
Terms:
  Resolution
    Number of bits an ADC gives as output
    Higher this number, finer the resolution of the ADC
  VREF
    Reference Voltage - maximum analog voltage that ADC will convert
    Voltages above this will be ‘saturated’
  Conversion time
    Time taken for a single conversion
    Depends on ADC clock, internal conversion circuitry, etc.
Data exchange:
  Analog input channel
    Pin / terminal for applying analog voltage to be converted
  Digital data output
    n-bit digital number output from the ADC in 1/more registers
Signals:
  Start conversion (GO)
    Signal to ADC to start the conversion
  End-of-conversion (DONE)
    Signal from ADC that conversion is completed

## Slide 8: ADC: System equations
Stepsize
Dout
VREF | Resolution | Stepsize
5V | 8-bits | 19.53mV
5V | 10-bits | 4.88mV
2V | 10-bits | 1.95mV
Vin | Stepsize | Dout
2V | 19.53mV | 102
4.5V | 4.88mV | 922
1V | 1.95mV | 512

## Slide 9: ADC: A graphical view
A plot of an ADC configuration – input and output side
Dout
Vin
…
VREF+
0
0
Stepsize
2*Stepsize
2resolution-1
Dynamic
Range
1
2
Saturation

## Slide 10: Electronics: An ADC calculator!
Handy ADC calculator – embedded Excel sheet

## Slide 11: PIC18F4520: In-built ADC
ADC circuitry
  13 analog input channels
    AN0 – AN12
  One 10-bit ADC
Analog channels need to be connected turn-by-turn
  13-way input multiplexing
  To be implemented in code (for loop)
Usage through:
  3 ‘config’ registers – ADCON0, ADCON1, ADCON2
  2 ‘result’ registers – ADRESH, ADRESL

## Slide 12: PIC18F4520: ADC pins – ANx, VREF

## Slide 13: PIC18F4520: ADCON0
CHS<3:0>: Analog input channel select bits
  0000: AN0
  0001: AN1
  …
  1100: AN12
  1101 to 1111: Not implemented
GO/DONE: ADC conversion status bit
  1: ADC conversion in progress
  0: ADC done/idle
ADON: ADC module ON bit
  1: On, 0: Off
-
-
CHS3
CHS2
CHS1
CHS0
GO/
DONE
ADON

## Slide 14: PIC18F4520: ADCON1
VCFG1: Voltage reference config bit (VREF- source)
  1: VREF- (AN2), 0: VSS
VCFG0: Voltage reference config bit (VREF+ source)
  1: VREF+ (AN3), 0: VDD
PCFG<3:0>: Port configuration control bits
D
E
F
R
-
-
VCFG1
VCFG0
PCFG3
PCFG2
PCFG1
PCFG0

## Slide 15: PIC18F4520: ADCON2
ADFM: Output justification bit (10 out of 16-bit ADRESH:ADRESL)
  0: left, 1: right
ACQT<2:0>: Automated acquisition time bits
  000: 0TAD
  001: 2TAD
  010: 4TAD
  …
  111: 20TAD
ADCS<2:0>: ADC conversion clock selection bits
  000: FOSC/2
  001: FOSC/8
  010: FOSC/32
  100: FOSC/4
  101: FOSC/16
  110: FOSC/64
  010, 111: FRC
ADFM
-
ACQT2
ACQT1
ACQT0
ADCS2
ADCS1
ADCS0

## Slide 16: PIC18F4520: ADC Block Usage
ADC usage steps
  ADCON1
    PCFG values (A/D),
    Reference voltages (VREF)
  ADCON0
    Input channel (ANx)
  ADCON2
    Justification (ADFM)
    Acquisition Time (ACQT)
    Clock (ADCS)
  ADCON0
    Put ADC ON (ADON)
  ADCON0
    Start conversion (GO/DONE)
  Gather output
    ADRESH:ADRESL
√
√
ADRESH
ADRESL
√
right
left

## Slide 17: PIC18F: ADC Summary
ADC
  Concept
  Advantages, Limitations
PIC18F4520 ADC
  Details
  Usage
  Output in
    ADRESH:ADRESL (10 out of 16 bits)
    Needs to be used appropriately
Inbuilt ADC (low-end real-world circuits)
  Saves cost
  Reduces power
  Minimizes PCBA real-estate

## Slide 18: Thank you!