## Slide 1: The PIC microcontroller
PIC18F4520: CCP and ECCP

## Slide 2: PIC18F: Controller Architecture

## Slide 3: PIC18F: Notational convention
WREG
  W Register
FREG
  File Register (any register location from GPR Bank 0 / SFR)
[X]
  Contents of register X
    [WREG] = 0x02 ↔ WREG’s contents become 0x02
    [0x20] = 0x34 ↔ RAM File Register 0x20 content becomes 0x34
    [X] = [Y] ↔ Contents of Y are copied into X
Number systems
Decimal | d’10’
Hexadecimal | h’4A’ or 0x4A
Binary | b’1000 0010’

## Slide 4: CCP concept

## Slide 5: PIC18F: CCP Module
PIC has a unique hardware module called CCP
  Tri-function module
    Compare
    Capture
    PWM
Used for control of hardware interfaces / devices
  Compare
    Complex automated if-then output signal to hardware
  Capture
    Free-running edge-detection, time snapshotting
  PWM
    Precise (2 decimal places!) CPU-independent PWMs
PIC18F4520 has 2 CCP modules
  CCP1, CCP2
In addition
  CCP1 can work as an ECCP (Enhanced CCP) module

## Slide 6: PIC18F: What is CCP?
Compare
  Compare a TIMER register to a pre-loaded CCPR register
  On value match, control a CCP pin (output) – rise, fall, toggle, etc.
Capture
  With a TIMER running, ingest a signal at a CCP pin (input)
  Capture value of TIMER register into CCPR register on an interesting event in the signal – rising edge / falling edge
PWM
  Using a TIMER, generate a precise PWM wave at CCP pin (output)
  Frequency and Duty Cycle controlled by CCPR register

## Slide 7: CCP1 on PIC18F4520

## Slide 8: PIC18F: CCP1 Details
CCP1 module resources
  Registers:
    Configuration, control: CCP1CON
    Timer selection: T3CON
    CCPR register: CCPR1H:CCPR1L (16-bit)
    PWM: PR2 (8-bit)
  Timer(s):
    Compare/Capture mode: Timer1 / Timer3
    PWM mode: Timer2
  Hardware pin(s):
    CCP1 / RC2
    T13CKI (clock input for chosen timer)

## Slide 9: PIC18F: CCP1CON
CCP1M<3:0>: CCP1 mode select bits
  0000 CCP1 is off / disabled
  0001 Reserved
  0010 Compare mode – Toggle CCP1 on match
  0011 Reserved
  0100 Capture mode – every falling edge
  0101 Capture mode – every rising edge
  0110 Capture mode – every 4th rising edge
  0111 Capture mode – every 16th rising edge
  1000 Compare mode – CCP1 init low, match high, CCP1IF set
  1001 Compare mode – CCP1 init high, match low, CCP1IF set
  1010 Compare mode – Generate s/w interrupt, CCP1 no effect
  1011 Compare mode – Special event, CCP1IF set, timer cleared
  11xx PWM mode
DC1B<1,2>: Duty cycle fractional part control bits for PWM
  Used only in PWM mode
-
-
DC1B1
DC1B2
CCP1M3
CCP1M2
CCP1M1
CCP1M0

## Slide 10: PIC18F: CCP1 – Timer selection
CCP1 choice of Timers
  Compare / Capture modes – Timer1 / Timer3
  PWM – Timer2 only
Compare / Capture Timer chosen by bits in T3CON
  T3CCP<2:1>: Timer selection bits for CCP modules
    00 Use Timer1 for both CCP modules
    01 Use Timer1 for CCP1, and Timer3 for CCP2
    1x Use Timer3 for both CCP modules
Chosen Timer controlled by corresponding TxCON
RD16
T3CCP2
T3CKPS1
T2CKPS2
T3SYNC
TMR3CS
TMR3ON
T3CCP1

## Slide 11: CCP1 compare mode

## Slide 12: PIC18F: CCP1 – Compare mode
TMR1H
TMR1L
CCPR1H
CCPR1L
CCP1
Logic
Compare
CCP1IF
Reset TIMER
Set IF
CCP1/RC2 pin
CCP1 interrupt
CCP1M3
CCP1M2
CCP1M1
CCP1M0
Effect
Pre-loaded
Ticking!
T1CON
Control
Match

## Slide 13: PIC18F: CCP1 – Compare details
Control the behaviour of the CCP1 pin (output)
  When there is a “Compare Match”
  When [CCPR1H:CCPR1L] == [TMR1H:TMR1L]
This happens once in the cycle of TMR1 when it ‘ticks’
  In its journey from 0x0000 to 0xFFFF
Behaviour controls
  Drive CCP1 from low to high – positive edge/pulse
  Drive CCP1 from high to low – negative edge/pulse
  Toggle CCP1
  Generate a software interrupt, and set CCP1IF
  Trigger a special event in hardware, and reset the timer

## Slide 14: PIC18F: CCP1 – Compare usage
Configure
  Initialize CCP1CON for proper compare mode
  Select Timer by writing to T3CON
  Configure chosen Timer (by writing T1CON / T3CON)
  Make CCP1/RC2 output (say, BCF TRISC, 2)
Load
  Load CCPR registers (CCPR1H:CCPR1L)
  Load Timer registers (TMR1H:TMR1L or TMR3H:TMR3L)
  Reset CCP1IF
Start
  Start Timer (TMR1 / TMR3)
Monitor / Service
  CCP1IF flag / CCP1 interrupt

## Slide 15: PIC18F: CCP1 – Compare code
Make CCP1 toggle on compare match for CCPR1 value of 0x1234
MOVLW 0x02
MOVWF CCP1CON ; compare mode, toggle on match
CLRF T3CON ; choose TIMER1
CLRF T1CON ; 16-bit, Internal CLK, 1:1 prescale, etc.
BCF TRISC, 2 ; make CCP1 / RC2 output
MOVLW 0x12
MOVWF CCPR1H
MOVLW 0x34
MOVWF CCPR1L ; load CCPR1 with value
L1 CLRF TMR1H
CLRF TMR1L
BCF PIR1, CCP1IF ; reset CCP1IF
BSF T1CON, TMR1ON ; start TIMER1
L2 BTFSS PIR1, CCP1IF ; monitor CCP1IF
BRA L2
BCF T1CON, TMR1ON ; stop TIMER1
BRA L1
0x0000
…
…
0x1234
…
...
0xFFFF
TMR1H:L
toggle

## Slide 16: Ccp1 capture mode

## Slide 17: PIC18F: CCP1 – Capture mode
TMR1H
TMR1L
CCPR1H
CCPR1L
CCP1
Logic
CCP1IF
Set IF
CCP1/RC2 pin
Capture
Counting!
Value
External Signal
Edge detect
CCP1M3
CCP1M2
CCP1M1
CCP1M0
T1CON
Control
Edge*
Capture
* Rising, falling, 4th rising, 16th rising

## Slide 18: PIC18F: CCP1 – Capture details
Ingest a signal at CCP1/RC2 pin (input)
Start a TIMER
  While this TIMER is running (‘ticking’)
    Detect pattern of interest
    On detection
      Capture the value of its TIMER register (TMRxH:TMRxL)
      Into CCPR1H:CCPR1L
Choices for pattern of interest
  Rising edge
  Falling edge
  Every 4th rising edge
  Every 16th rising edge
Snapshot when pattern occurred

## Slide 19: PIC18F: CCP1 – Capture usage
Configure
  Initialize CCP1CON for proper capture mode
  Select Timer by writing to T3CON
  Configure chosen Timer (by writing T1CON / T3CON)
  Make CCP1/RC2 input (say, BSF TRISC, 2)
  Reset CCP1IF
  Reset Timer registers (TMR1H:TMR1L or TMR3H:TMR3L)
Wait-1
  Wait for pattern of interest to occur at CCP1 (monitor CCP1IF)
Load & Start
  Start Timer (TMR1 / TMR3)
Wait-2
  Wait for pattern of interest to occur at CCP1 (monitor CCP1IF)
Read values
  Stop Timer (TMR1 / TMR3)
  Read the captured value of CCPR1H:CCPR1L
T
Timer start
Timer stop
T = n * TTMR

## Slide 20: PCI18F: CCP1 – Capture code
Measure the period of input pulse applied at CCP1/RC2
MOVLW 0x05
MOVWF CCP1CON ; capture mode, rising edge
CLRF T3CON ; choose TIMER1
CLRF T1CON ; 16-bit, Internal CLK, 1:1 prescale, etc.
BSF TRISC, 2 ; make CCP1/RC2 input
CLRF TMR1H
CLRF TMR1L
BCF PIR1, CCP1IF ; clear IF
RISE1 BTFSS PIR1, CCP1IF ; wait for 1st rising edge
BRA RISE1
BCF PIR1, CCP1IF ; 1st edge detected, clear IF
BSF T1CON, TMR1ON ; start TIMER1
RISE2 BTFSS PIR1, CCP1IF ; wait for 2nd rising edge
BRA RISE2
BCF T1CON, TMR1ON ; 2nd edge detected, stop TIMER1
GOTO $
CCPR1H:CCPR1L contain ticks counted by TIMER1

## Slide 21: Ccp1 pwm mode

## Slide 22: PIC18F: CCP1 – PWM mode
TMR2H
TMR2L
PR2
CCPR1L
CCP1
Logic
Load TIMER
CCP1/RC2 pin
CCP1M3
CCP1M2
CCP1M1
CCP1M0
PWM
Loaded with values
DC1B1
DC1B2
T2CON
Control
Ticking!
Timer ON

## Slide 23: PIC18F: CCP1 – PWM details
Hardware controlled generation of PWM
  Waveform appears at CCP1/RC2 pin (output)
  Uses TIMER2
  Precise control of frequency and Duty Cycle (DC)
    DC control up to 2 decimal places!
PWM control registers
  Frequency control
    PR2 (8-bit) register – is in SFR
    Pre-scale ratio of TIMER2
  DC control
    CCPR1L (integer part), DC1B1, DC1B2 (fractional part)

## Slide 24: PIC18F: CCP1 – PWM equations
Generate a PWM of frequency and DC of
  Frequency
  Start with N=1
  If PR2>255, try N=4, then N=16
  DC
  Calculate
    given by
yFRACTION | DC1B2 | DC1B1
0 | 0 | 0
0.25 | 0 | 1
0.50 | 1 | 0
0.75 | 1 | 1

## Slide 25: PIC18F: CCP1 – PWM scenarios
Generate a PWM of 10kHz and 55% DC, Fosc = 10MHz
  PR2<255, hence pre-scaler=1:1
Generate a PWM of 1kHz and 35% DC, Fosc = 10MHz
  PR2>255, so try pre-scaler=1:1, 1:4, 1:16

## Slide 26: PIC18F: CCP1 – PWM usage
Pre-calculate
  PR2, pre-scaler for TIMER2, CCPR1L, DC1B2:DC1B1
Configure CCP1CON for PWM mode
  Load DC bits as well
Load PR2
Configure T2CON
Load CCPR1L
Make CCP1/RC2 an output pin
Clear TMR2H:TMR2L
Start TIMER2

## Slide 27: PIC8F: CCP1 – PWM code
Generate a PWM of 1kHz and DC 35% at CCP1
MOVLW 0x1C
MOVWF CCP1CON ; PWM mode, 0.25% DC bits
MOVLW d’155’
MOVWF PR2 ; 1kHz fPWM
MOVLW 0x03
MOVWF T2CON ; 1:16 pre-scaler
MOVLW 0x36
MOVLW CCPR1L ; yINTEGER
BCF TRISC, 2 ; make CCP1 / RC2 output
CLRF TMR2H
CLRF TMR2L ; clear TIMER2
BSF T2CON, TMR2ON ; start TIMER2
GOTO $

## Slide 28: Electronics: PWM use-cases
Myriad applications require a precise, good quality PWM
  Light intensity control (dimming feature)
  Motor speed control
  Telecommunications (signal transmission, reception)
  Consumer AV: Audio effects and amplification
  Power delivery: Electric cookers, ovens, etc.
  Fan speed control
  Servomechanism control: Valves, motors, etc.
  Voltage regulators
  Solar tracking and charging systems

## Slide 29: Bi-Directional speed control of dc motors

## Slide 30: Electronics: H-Bridge for Direction control
Direction Control is realized through ‘H-bridge’
Switches 1, 2, 3, 4 are high-speed, high-current switches
  A CPU drives them to give directional speed control
Control can be achieved by
  Half-bridge configuration
  Full-bridge configuration

## Slide 31: Electronics: H-Bridge operation
Clockwise rotation
Switches 1, 4 closed
Switches 2, 3 open
Anticlockwise rotation
Switches 1, 4 open
Switches 2, 3 closed

## Slide 32: ECCP

## Slide 33: PIC18F: ECCP – what is it?
ECCP stands for Enhanced CCP
  Compare and Capture modes remain as is
  PWM gets enhanced (2/4 signal PWM)
PIC18F4520 CCP1 module can work in ECCP mode
CCP1 ECCP use-cases
  Bi-directional speed control of DC Motors
  Gives 3-pronged control:
    On/Off, Speed, Direction
  Supports both configurations
    Half-bridge
    Full-bridge

## Slide 34: PIC18F: ECCP PWM Pin-out
Up to 4-pin PWM: P1A, P1B, P1C, P1D

## Slide 35: PIC18F: CCP1 – ECCP
ECCP-mode CCP1CON
P1M<1:0>: Enhanced PWM output configuration bits
  Only when CCP1M3:0 are 11xx
  00 Single-output PWM on P1A (P1B, P1C, P1D as port pins)
  01 Full-bridge output forward
    P1D PWM, P1A active
    P1B, P1C inactive
  10 Half-bridge output
    P1A and P1B PWM
    P1C, P1D as port pins
  11 Full bridge output reverse
    P1B PWM, P1C active
    P1A, P1C inactive
P1M1
P1M0
DC1B1
DC1B2
CCP1M3
CCP1M2
CCP1M1
CCP1M0

## Slide 36: PIC18F: ECCP1 – FB PWM (fwd)
Forward: P1D PWM, P1A active, P1B, P1C inactive
PWM

## Slide 37: PIC18F: ECCP1 – FB PWM (rev)
Reverse: P1B PWM, P1C active, P1A, P1D inactive
PWM

## Slide 38: PIC18F: ECCP1 – HB PWM
Half-bridge: P1A and P1B both PWM

## Slide 39: PIC18F: CCP Summary
CCP
  Concept
  CCP details in PIC18F4520
    Compare
    Capture
    PWM
PWM use-cases
Bidirectional speed control using H-bridge
CCP1 in ECCP mode
  Half and Full bridge configurations

## Slide 40: Thank you!