## Slide 1: The PIC microcontroller
PIC18F4520: Serial Buses (UART, I2C, SPI)

## Slide 2: PIC18F: Controller Architecture

## Slide 3: PIC18F: Notational convention
WREG
  W Register
FREG
  File Register (any register location from GPR Bank 0 / SFR)
[X]
  Contents of register X
    [WREG] = 0x02 ↔ WREG’s contents become 0x02
    [0x20] = 0x34 ↔ RAM File Register 0x20 content becomes 0x34
    [X] = [Y] ↔ Contents of Y are copied into X
Number systems
Decimal | d’10’
Hexadecimal | h’4A’ or 0x4A
Binary | b’1000 0010’

## Slide 4: Interfaces parallel, serial

## Slide 5: Electronics: Parallel Interface
What
  Signal is transmitted on several lines
    Signal bits spread out – in sync, in parallel
Pros
  Higher speed of transmission (throughput)
    Due to multiple lines carrying bits
  Simpler to code
    Since register lengths map out to signal lines
Cons
  Very high cost (in terms of pin and PCBA-layout real estate)
  High ISI (inter signal interference) - due to line proximity
  Signal boosting (for long distance travel) is expensive

## Slide 6: Electronics: Serial interface
What
  Signal is transmitted on a single line (not counting ground)
    Signal bits sent out one after another – serially
Pros
  Much lower cost due to lesser number of lines
  No ISI (inter signal interference)
  Signal boosting (for long distance travel) is simpler
Cons
  Low throughput
    Has to be boosted using very high speed clocks
  Handshake options have to be pre-determined
    LSB-first / MSB-first, etc.
  Challenge to code
    Need to handle SerDes (serializing – deserializing)

## Slide 7: Electronics: Serial – Transmission modes
Simplex
  One-way communication
  Only one device talks, the other only listens
Half-duplex
  Two-way communication
  Both devices can talk, but only one at a time
Full-duplex
  Two-way communication
  Both devices can talk simultaneously

## Slide 8: Electronics: Serial – Signaling
Synchronous
  Has a Reference Clock
  Additional expense!
Asynchronous
  No Clock signal
  Extra START/STOP markers!
  Data rate vs Baud rate
Pay-load

## Slide 9: Serial bus – uart (RS-232)

## Slide 10: UART: The RS-232 standard
UART: Universal Asynchronous Receiver Transmitter
RS-232: Recommended Standard #232
  Defined in 1960 as a serial communication standard
  Intended for signaling between DTE (PC) and DCE (modem)
  Original standard defined 25 signals, but only 3 are used today
    RX (Receive), TX (Transmit), GND (Ground)
  Connectors:
    Old: DB-25, New: DB-9, Current: None (Use a USB-Serial adapter!)
Female
Male

## Slide 11: RS-232: Bus wiring
Device 1’s RX will go into Device 2’s TX
  And vice-versa
Common ground

## Slide 12: RS-232: Bus voltages, MCU interfacing
RS-232 voltage levels TTL voltage levels
+25V
+3V
-3V
-25V
0V
0.8V
2V
5V
Logic 0
Logic 1
Logic 0
Logic 1
Level shifting
(MAX232)

## Slide 13: RS-232: Bus Nomenclature
Terminology
Baud Rate
  Speed at which data travels
  Most common: 9600 baud
Payload size
  Size of ‘data payload’
  Most common: 8-bit
Parity
  Extra bits added for reducing effects of noise
  Odd (O), Even (E) or None (N)
Stop bits
  Extra bits to serve as stop markers
  Note: Start marker is always 1-bit
Examples
9600/8-N-1
57600/8-E-1
115200/8-O-2
10-bit packet
11-bit packet
12-bit packet

## Slide 14: RS-232: Limitations
Old standard
  Pre-dates most computer technologies
Large connectors
  Out of place with today’s equipment
Low noise immunity
  Due to single-ended signaling
Low transmission speed
  Less throughput
Short maximum cable length
  ~15m (subject to noise conditions and line capacitance)
Large voltages and voltage swings
  TTL-incompatible, needs drivers
No multi-point capability
  Point-to-point (P2P) bus
Limited multi-drop capability
  Non-standard, unstable

## Slide 15: Uart/rs-232 on pic18f

## Slide 16: PIC18F: UART/RS-232
UART is realized through dedicated hardware module
UART resources
  Registers
  Pins
    TX/RC6, RX/RC7
  IF flags and IE flags
    TXIF, RCIF (part of PIR1)
    TXIE, RCIE (part of PIE1)
TXSTA | Transmit status and control
RCSTA | Receive status and control
TXREG | Transmit register
RCREG | Receive register
SPBRGH:SPBRG | Baud rate (speed) control

## Slide 17: PIC18F: UART – TXSTA
CSRC: Clock source select bit (Don’t care in Async mode)
TX9: 9-bit transmit enable bit
TXEN: Transmit mode enable bit
SYNC: Mode select bit
  0: Async, 1: Sync
SENDB: Send break character bit
BRGH: High baud rate select bit
  0: Low speed, 1: High speed
TRMT: Transmit shift register status bit
  0: Full, 1: Empty
TX9D: 9th bit in 9-bit transmit mode
CSRC
TX9
TXEN
SYNC
SENDB
BRGH
TRMT
TX9D
Value for Async mode Transmit: 0x20

## Slide 18: PIC18F: UART – RCSTA
SPEN: Serial port enable bit
RX9: 9-bit receive enable bit
SREN: Single receive enable bit
  Aysnc mode: Don’t care
CREN: Continuous receive enable bit
ADDEN: Address detect enable bit (9-bit)
FERR: Framing error bit
  0: No framing error, 1: Framing error occurred
OERR: Overrun error bit
  0: No overrun error, 1: Overrun error occurred
RX9D: 9th bit of 9-bit receive mode
SPEN
RX9
SREN
CREN
ADDEN
FERR
OERR
RX9D
Value for Async mode Receive: 0x90

## Slide 19: PIC18F: UART – Baud rate formulas
Baud rate of the UART port is determined by:
  Values of
    BRGH (TXSTA, bit 2) and BRG16 (BAUDCON, bit 3)
  Contents of
    SPBRGH:SPBRG registers (say, )
BRG16 | BRGH | UART mode | Baud rate formula
0 | 0 | Async, 8-bit | 
0 | 1 | Async, 8-bit | 
1 | 0 | Async, 16-bit | 
1 | 1 | Async, 16-bit | 
BRG16 | BRGH | UART mode | Baud rate formula
0 | 0 | Async, 8-bit | 
0 | 1 | Async, 8-bit | 
1 | 0 | Async, 16-bit | 
1 | 1 | Async, 16-bit | 

## Slide 20: PIC18F: UART – Transmit mode
Steps
Enable transmit
  Load TXSTA (0x20)
Determine speed
  Load SPBRG’s, BRG16
Fix TX pin direction
  Make TX/RC6 output
Clear IF flag
  TXIF bit of PIR1
Enable serial port
  SPEN bit of RCSTA
Load TXREG with data
Check for transmit complete
Schematic
PIC18F4520
TX/RC6
TXREG
TSR
FREG
TXSTA
RCSTA
TXIF

## Slide 21: PIC18F: UART – Receive mode
Steps
Enable serial port, and continuous receive
  Load RCSTA (0x90)
Determine speed
  Load SPBRG’s, BRG16
Fix RX pin direction
  Make RX/RC7 input
Clear IF flag
  RCIF bit of PIR1
Wait for data reception
  Monitor RCIF REG with data
Data available in RCREG!
Schematic
PIC18F4520
RX/RC7
RCREG
RSR
FREG
RCSTA
RCIF

## Slide 22: PIC18F: UART – Experiment topology
PIC dev board connected to PC’s serial port (COMx)
PC running serial port software: PuTTY / Hyper-terminal
PIC code should enable
  UART Receive (data from PC)
  UART Transmit (echo back data so received)
PIC18F4520
ABC…
RX
TX
UART code
TXREG
RCREG
Serial cable

## Slide 23: Serial bus – i2c

## Slide 24: I2C: The Standard
I2C: Inter Integrated Circuit
  Defined by Philips (now NXP) in 1982 as a serial bus
  Synchronous, Multi-master, Multi-slave
  Multi-drop, Packet-switched, Half-duplex
  Single-ended: 2 pins with 2 signals
    SCL (System Clock), and SDA (System Data)
I2C: Wiring
  No standards defined
  Bus length limited by bus capacitance (<400pF)
  Open-Collector / Open-Drain pins
I2C: Voltages
  TTL compatible
    Logic 1: 5V, 3.3V
    Logic 0: 0V

## Slide 25: I2C: Use-cases, speeds
Intended use
  Popular bus for connecting peripheral devices to controllers / CPUs
    Interacting with compatible EEPROMs, RTCs, NVRAM chips, …
    Controlling low-speed ADCs, DACs
    Controlling display properties (contrast, hue, colour balance) via DDC
    Controlling low-end OLED / LCD displays
    Interfacing with compatible sensors
    System Management (via SMBus avatar)
Speeds
  Standard (100 kbits/s)
  Fast-mode (400 kbits/s)
  High-speed (3.4 Mbits/s)
  Ultra Fast-mode (5 Mbits/s)

## Slide 26: Electronics: Open collector / drain
Outputs left ‘floating’ (open)
  Pull-up resistor used to ‘pull up’ the line to Vcc
When outputs are different: OUT1=1 and OUT2=0
    Device sending 0 ‘wins’ over device sending 1
Open collector
Device 1
Device 2
Open drain
OUT2=0
OUT1=1
Result=0

## Slide 27: I2C: Open-collector / Open-drain
I2C Bus Topology
SCL and SDA lines are open-collector design
  Pulled up to VCC / VDD (Logic 1)
    Nothing to be done to send a Logic 1
  Pulled down to ground (0V) to send a Logic 0
  Device sending 0 ‘wins’ over device sending 1

## Slide 28: I2C: Roles, Addressing
I2C Roles: 2 distinct roles defined
  Master
    Initiates communication (called ‘transactions’)
    Drives the system clock (SCL)
    Performs bus arbitration
  Slave
    Responds to master
    Accepts data from master
    Send data when asked by master
I2C Addressing:
  Slaves need to have ‘addresses’ to exist on the bus
    8-bit (actually 7+1) / 10-bit
  Masters do not have addresses

## Slide 29: I2C: Signaling
I2C has special signals / sequences
  To signify start and end of transactions
  Combination of line (SCL, SDA) voltage conditions and waveforms
START sequence (symbol: “S”)
  SCL stays HIGH, SDA goes from HIGH to LOW
STOP sequence (symbol: “P”)
  SCL stays HIGH, SDA goes from LOW to HIGH

## Slide 30: I2C: SCL, SDA relationship
Pin-wise:
  SCL is Clock – Always driven by Master
  SDA is Data – Driven by Master/Slave
SDA is stable when SCL is HIGH
  Data is ‘sampled’ on the line by Master/Slave
SDA line is written MSB-first
  8-bit packets
    7-bit Slave address + 1 R/W bit
    8-bit data
  9th bit is driven LOW by other device as ACK

## Slide 31: I2C: Bus modes, Transaction types
I2C bus modes
  Master sending address/data to Slave
    Master drives SCL and in charge of SDA
  Slave sending data to Master
    Master drives SCL, Slave in charge of SDA
I2C transaction types
  I2C Write
    Master writes data to Slave
  I2C Read
    Master reads data from Slave

## Slide 32: I2C: Write Transaction – simple
Steps for an I2C Write (simple I2C Slave)
  Start
    Master sends START sequence
  Slave identification by Slave address (W)
    Master sends 7-bit Slave address (MSB-first)
    Master send R/W bit (value 0 – meaning write)
    Slave sends 1-bit ACK (value 0)
  Data send-out
    Master sends 8-bit data to Slave
    Slave sends 1-bit ACK (value 0)
  End
    Master sends STOP sequence

## Slide 33: I2C: Write Transaction – advanced
Steps for an I2C Write (memoried I2C Slave – EEPROM)
  Start
    Master sends START sequence
  Slave identification by Slave address (W)
    Master sends 7-bit Slave address (MSB-first)
    Master send R/W bit (value 0 – meaning write)
    Slave sends 1-bit ACK (value 0)
  Slave internal location address send-out
    Master sends 8-bit address of location inside Slave
    Slave sends 1-bit ACK (value 0)
  Data send-out
    Master sends 8-bit data to Slave
    Slave sends 1-bit ACK (value 0)
  End
    Master sends STOP sequence

## Slide 34: I2C: Advanced Write Illustration
Bus states for writing to I2C Slave – EEPROM
1
2
3
4
5

## Slide 35: I2C: Read Transaction – advanced
Steps for an I2C Read (memoried I2C Slave – EEPROM)
  Start
    Master sends START sequence
  Slave identification by Slave address (W)
    Master sends 7-bit Slave address (MSB-first)
    Master send R/W bit (value 0 – meaning write)
    Slave sends 1-bit ACK (value 0)
  Slave internal location address send-out
    Master sends 8-bit address of location inside Slave
    Salve sends 1-bit ACK (value 0)
  Slave identification by Slave address (R)
    Master sends 7-bit Slave address (MSB-first)
    Master send R/W bit (value 1 – meaning read)
    Slave sends 1-bit ACK (value 0)
  Slave data send-out
    Slave sends 8-bit data
    Master sends 1-bit NACK (value 1)
  Stop
Dummy Write

## Slide 36: I2C: Advanced Read Illustration
Bus states for reading from I2C Slave – EEPROM
1
2
3
4
6
5
Repeated START

## Slide 37: I2C: Clock Stretching
I2C devices
  Masters are usually high-speed controllers
  Slaves are usually low-speed devices
What if Slave can not keep up with Master?
Mechanism to let Slave ‘slow down’ the bus
  Slave pulls the SCL line low
  Master keeps a tab on the SCL line
    ‘Hold’ if it sees the SCL line held low
    Resume only when SCL returns to normal
  Since this ‘stretches’ the clock, it is called Clock Stretching
Uses the Open collector / drain property
  Device sending Logic 0 ‘wins’ over device sending Logic 1

## Slide 38: I2C: Bus Arbitration
Multi-master bus raises the question of Bus Arbitration
  What if 2 Masters start transacting at the same time?
Again, use is made of the Open collector / drain property
  Master sending 0 ‘wins’ over the Master sending 1
Master keeps a tab on SDA
  Compares what it sends to what it senses
    If it sent a 0 and got SDA LOW
      Everything is alright
    If it sent a 1 and got SDA HIGH
      Everything is alright
    If it sent a 1 and got SDA LOW
      Some other Master is driving the bus!
      This Master ‘loses’ Bus Arbitration and backs off
      Will restart the transaction once it senses a STOP
Smooth back-off ensuring no transactional data is ‘lost’

## Slide 39: I2C: Pluses and minuses
Pros
  More advanced compared to UART
    Multi-master, multi-slave, multi-drop
  Scalable bus due to open collector/drain logic
    Fans up to a dozen devices or so
  TTL compatible signalling
    Reduces system cost (no level shifting!)
  Natural bus arbitration scheme reduces system complexity
  Adjustable speed (flow control) through clock stretching
    Enables low-end Slave participation
Cons
  Complicated protocol with role-based transactions
  Low throughput due to:
    Overheads [START/STOP sequences, ACKs, address packets]
    Half-duplex operation
    Low speeds (kHz to 10’s of MHz)
  Lesser bus length compared to UART (< 5m, within board/PCBA)
    Could be remedied by I2C repeaters
  Low bus membership due to 7-bit addressing
  Pull-up resistors for SCL, SDA increase power dissipation
  Faulty / rogue device can hang the bus!

## Slide 40: i2c on pic18f

## Slide 41: PIC18F: I2C Resources
Hardware module (shared with SPI)
  MSSP – Master Synchronous Serial Port
MSSP Registers
Pins
  SCL/RC3, SDA/RC4
Flags
  SSPIF (part of PIR1)
SSPCON1, SSPCON2 | I2C bus control
SSPSTAT | I2C bus status
SSPADD | I2C bus speed
SSPBUF | I2C data register

## Slide 42: PIC18F: I2C – SSPCON1
WCOL: Write collision detect bit
  0: no collision; 1: a premature write was attempted to SSPBUF
SSPOV: Receive overflow indicator bit (in receive mode)
  0: no overflow; 1: overflow – new data arrived before SSPBUF cleared
SSPEN: MSSP module enable bit
CKP: SCL release control bit (Slave mode)
  0: Holds SCL LOW; 1: release SCL
SSPM<3:0>: MSSP mode select bits
  0110 I2C Slave mode, 7-bit address
  0111 I2C Slave mode, 10-bit address
  1000 I2C Master mode,
  1011 I2C firmware controlled Master
  1110 I2C Slave mode, 7-bit address, S-P interrupts enabled
  1111 I2C Slave mode, 10-bit address, S-P interrupts enabled
WCOL
SSPOV
SSPEN
CKP
SSPM3
SSPM2
SSPM1
SSPM0

## Slide 43: PIC18F: I2C – SSPCON2
GCEN: General call enable bit (Slave mode)
ACKSTAT: Acknowledge status bit (Master mode)
  0: ACK wasn’t received from Slave; 1: ACK was received
ACKDT: Acknowledge data bit (Master receive mode)
  0: ACK; 1: NACK
ACKEN*: Acknowledge enable (Master receive mode)
  0: Disabled; 1: Enabled (sends ACKDT to Slave)
RCEN: Receive enable bit (Master mode)
PEN*: STOP sequence enable bit (Master mode only)
RSEN*: Repeated START enable bit (Master mode only)
SEN*:
  Master mode: START sequence enable bit
  Slave mode: Clock Stretch enable bit
* Automatically cleared by hardware
GCEN
ACKSTAT
ACKDT
ACKEN
RCEN
PEN
RSEN
SEN
Master side (N)ACK

## Slide 44: PIC18F: I2C – SSPSTAT
SMP: Slew rate control bit
  0: Slew rate control enabled for high speed (400 kHz)
  1: Slew rate control disabled for standard speed (100 kHz, 1MHz)
CKE: SMBus select bit (SMBus mode)
D/A: Data / address indicator (in Slave mode)
P: STOP sequence detected (cleared on a reset)
S: START sequence detected (cleared on a reset)
R/W: In Master mode, 1 means transmit in progress
UA: Update address (10-bit address mode)
BF: Buffer full indicator bit
  0: empty, 1: full
SMP
CKE
D/A
P
S
R/W
UA
BF

## Slide 45: PIC18F: I2C – Bus speed, SSPBUF
Contents of SSPADD decide bus speed
  Bus speed is given by the following equation
SSPBUF is an 8-bit register
  Used for
    Sending address/data (Master send)
    Receiving data (Master receive, Slave send)
  Similar to TXREG and RCREG in UART!

## Slide 46: PIC18F: I2C – Code snippets
I2C initialization sequence
; 20MHz crystal, 100kHz
SPD_VAL EQU 0x49
BSF SSPSTAT, 7 ; sampling
BCF SSPSTAT, 6 ; slew rate disabled
MOVLW SPEED_VAL
MOVWF SSPADD ; loading SSPADD
; Master mode
BSF SSPCON1, SSPM3
BCF SSPCON1, SSPM2
BCF SSPCON1, SSPM1
BCF SSPCON1, SSPM0
BCF PIR1, SSPIF ; clear SSPIF
BSF SSPCON1, SSPEN ; enable MSSP module
START, STOP, SEND functions
I2CSTART
BSF SSPCON2, SEN
BTFSS PIR1, SSPIF
GOTO $-1
BCF PIR1, SSPIF
RETURN
I2CSTOP
BSF SSPCON2, PEN
BTFSS PIR1, SSPIF
GOTO $-1
BCF PIR1, SSPIF
RETURN
I2CSEND
MOVWF SSPBUF
BTFSS PIR1, SSPIF
GOTO $-1
BCF PIR1, SSPIF
RETURN

## Slide 47: PIC18F: I2C – Code snippets - Write
Assumes data to be sent is in WREG
TMP EQU 0x20
I2CWRITE
MOVWF TMP ; save WREG contents away
CALL I2CSTART ; generate START sequence
MOVLW <SLAVE_ADDR> ; Slave address with WRITE enabled
CALL I2CSEND
MOVLW <SLAVE_LOCATION> ; address location inside Slave
CALL I2CSEND
MOVF TMP, W ; send data to Slave
CALL I2CSEND
CALL I2CSTOP ; generate STOP sequence
RETURN

## Slide 48: PIC18F: I2C – Code snippets - Read
Data read in from Slave will be in WREG
I2CREAD
CALL I2CSTART ; generate START sequence
MOVLW <SLAVE_ADDR> ; Slave address with WRITE enabled
CALL I2CSEND
MOVLW <SLAVE_LOCATION> ; address location inside Slave
CALL I2CSEND
CALL I2CSTART ; repeated START
MOVLW <SLAVE_ADDR1> ; Slave address with READ enabled
CALL I2CSEND
BSF SSPCON2, RCEN ; enable Master receive mode
BTFSS PIR1, SSPIF ; wait for data reception (from Slave)
GOTO $-1
BCF PIR1, SSPIF
BSF SSPCON2, ACKEN ; enable Master ACK mode
BSF SSPCON2, ACKDT ; send a NACK from Master
MOVF SSPBUF, W
CALL I2CSTOP ; generate STOP sequence
RETURN

## Slide 49: Serial bus – spi

## Slide 50: SPI – The Standard
SPI: Serial Peripheral Interface
  Defined by Motorola in the early 1980s, now a de facto standard
  Synchronous, Single-master, Multi-slave
  Multi-drop, Full-duplex, High-speed bus
  4-wire / 4-pin signalling
    SCLK (Serial Clock), SS (Slave Select) – active low
    MOSI (Master Out Slave In), MISO (Master In Slave Out)
SPI wiring, voltages
  No standards defined, TTL compatible
  High speed restricts bus lengths (intra-board)

## Slide 51: SPI: Use-cases, speeds
Intended use
  Popular bus for connecting peripheral devices to controllers / CPUs
    Sensors (temperature, pressure), ADCs, touchscreens
    Control devices – audio codecs, digital pots, DACs
    Camera lens and mount assemblies
    Communications – ethernet, USB, CAN, IEEE 802.15.4, IEEE 802.11
    Memories – flash, EEPROM (specially for boot-up)
    Memory cards – MMC, SD Card
    RTCs
    LCDs (control - and sometimes, data)
Speeds
  Absence of defined protocols and packet structure
    Enables very high bus speeds (kHz to 100’s of MHz)

## Slide 52: SPI: Device Roles
SPI Roles: 2 distinct roles defined
  Master
    Initiates communication (called ‘data frame’)
    Drives the system clock (SCLK)
    Selects a Slave by using the per-Slave active LOW SS line
  Slave
    Responds to master if it’s SS line is active
    Full-duplex
      Can receive from, as well as send to Master
Single Master, multiple Slaves bus
No defined packet / frame protocol
  Designer free to select appropriate sized frames

## Slide 53: SPI: Bus topologies
Single Master, Single Slave
  Master drives SCLK
  Selects Slave by SS line
    Optional since only 1 Slave
      Hard-wire SS to 0!
  Half or Full duplex operation
Single Master, Multiple Slaves
  Master drives SCLK
  Selects Slave by SS line
    1 SS line per Slave!
  Slaves share SCLK, MISO, MOSI lines
    Non-participating Slaves need to tri-state these lines!
  Half or Full duplex operation

## Slide 54: SPI: Bus operation
Master selects the Slave by de-asserting its SS line
  For ‘slow’ devices, Master waits for a hold time
Master activates the clock on SCLK line
Full-duplex data transfer occurs
  Master sends out a bit on MOSI, Slave receives it
  Slave sends out a bit on MISO, Master receives it
  Transmission occurs between n-bit registers in Master and Slave
    Connected in a ‘virtual ring’ topology
  Slave always sends data – not all transfers may be of value!

## Slide 55: SPI – Line Waveform example
General line waveform
  Master-Slave communication
  Full-duplex, 8-bit communication
    O<7:0> – Master to Slave
    I<7:0> – Slave to Master

## Slide 56: SPI: Pros and Cons
Pros
  Very high throughput
    High-speed, Full-duplex bus
  Protocol flexibility
    Arbitrary choice of word length (8/16/32/64…)
  Simple hardware interfacing
    No pull-up resistors
  No arbitration messiness
  No addressing complexities / restrictions
Cons
  Rather costly
    4-wire interface – high PCB real estate
    1 SS line per Slave!
  Restricted to a single master
  No support for flow control by Slave
  No error checks / parity included by default (has to be in software)
  Difficult to add Slave devices
    Usually needs a PCB respin!

## Slide 57: Spi on pic18f

## Slide 58: PIC18F: SPI Resources
Hardware module (shared with I2C)
  MSSP – Master Synchronous Serial Port
MSSP Registers
Flags
  SSPIF (part of PIR1)
SSPCON1 | SPI bus control
SSPSTAT | SPI bus status
SSPBUF | SPI data register

## Slide 59: PIC18F: SPI Resources – Pins
SCLK = SCK/RC3, MOSI = SDI/RC4, MISO = SDO/RC5
SS = Any IO pin (Master mode), SS/RA5 (Slave mode)

## Slide 60: PIC18F: SPI – SSPCON1
WCOL: Write collision detect bit
  0: no collision; 1: a premature write was attempted to SSPBUF
SSPOV: Receive overflow indicator bit (in Slave mode)
  0: no overflow; 1: overflow – new data arrived before SSPBUF cleared
SSPEN: MSSP module enable bit
CKP: Clock polarity select bit
  0: Idle is LOW; 1: Idle is high
SSPM<3:0>: MSSP mode select bits
  0000 SPI Master mode, Clock = Fosc/4
  0001 SPI Master mode, Clock = Fosc/16
  0010 SPI Master mode, Clock = Fosc/64
  0011 SPI Master mode, Clock = TMR2 output/2
  0100 SPI Slave mode, Clock = SCK pin, SS pin control enabled
  0101 SPI Slave mode, Clock = SCK pin, SS pin control disabled
WCOL
SSPOV
SSPEN
CKP
SSPM3
SSPM2
SSPM1
SSPM0

## Slide 61: PIC18F: SPI – SSPSTAT
SMP: Sample bit (Master mode, disabled [0] for Slave mode)
  0: Input sampled at middle of data output time
  1: Input sampled at end of data output time
CKE: SPI Clock select bit
  0: Transmit on idle to active clock transition
  1: Transmit on active to idle clock transition
D/A: Unused
P: Unused
S: Unused
R/W: Unused
UA: Unused
BF: Buffer full indicator bit (receive mode)
  0: SSPBUF is empty, 1: receive complete, SSPBUF is full
SMP
CKE
D/A
P
S
R/W
UA
BF

## Slide 62: PIC18F: SPI – Master-Slave connects
2 PIC18Fs – one Master, another Slave
Internal ‘virtual-ring’ between Master-Slave

## Slide 63: PIC18F: SPI – Clock Edge Signalling
SCLK, CKE, CKP and SMP relationships

## Slide 64: PIC18F: SPI code snippet – Master
PIC as SPI Master (Full duplex), assumes Slave connected via RC2
DAT EQU 0xAB
BCF TRISC, 3 ; SCLK output
BCF TRISC, 4 ; SDO output
BSF TRISC, 5 ; SDI input
CLRF SSPSTAT ; Idle to Active Clock, BF to zero
MOVLW 0x20
MOVWF SSPCON1 ; Enable MSSP, Master, Fosc/4, idle LOW
BCF TRISC, 2 ; Set Slave’s SS line low
MOVLW DAT
MOVWF SSPBUF ; data to Slave
BTFSS SSPSTAT, BF ; wait for BF to go high
GOTO $-1
BSF TRISC, 2 ; disable Slave’s SS line
MOVWF SSPBUF, W ; data from Slave

## Slide 65: PIC18F: SPI code snippet – Slave
PIC as SPI Slave in Receive mode
BSF TRISC, 3 ; SCLK input
BCF TRISC, 4 ; SDO output
BSF TRISC, 5 ; SDI input
BSF TRISA, 5 ; SS for Slave mode
CLRF SSPSTAT ; Idle to Active Clock, BF to zero
MOVLW 0x24
MOVWF SSPCON1 ; Enable MSSP, Slave, SS enabled
BTFSS SSPSTAT, BF ; wait for BF to go high
GOTO $-1
MOVWF SSPBUF, W ; data from Master

## Slide 66: PIC18F: Serial Interfaces Summary
Serial vs. Parallel
  Concepts
  Pros and Cons
Serial interfaces
  Signaling
  Serial buses
    UART/RS-232, I2C, SPI
      Bus standards
      Physical layer
        Wiring, Voltages, Topologies
      Packet formats and protocols
      Merits and demerits, comparisons
    PIC18F implementations and usage models
      UART/RS-232 hardware module
      MSSP

## Slide 67: Thank you!