## Slide 1: rtos
Introduction

## Slide 2: Basic concepts

## Slide 3: Concepts: Events, classifications
Event
  An occurrence that changes program flow non-sequentially
Event classification 1
Event classification 2
Deterministic system
  For each possible state and input, a unique output and next state can be determined
Synchronous events | Asynchronous events
Occur at predictable times In sync with code | Occur at unpredictable times Not in sync with code
Periodic events | Aperiodic events | Sporadic events
Repeat at precise, regular times | Repeat, but not at regular periods | Appear infrequently, at irregular times

## Slide 4: Concepts: Events – Examples
 | Periodic | Aperiodic | Sporadic
Synchronous | - Cyclic code - Processes scheduled by internal clock | - Branches - Jumps - Garbage collection | - Error recovery code - System calls
Asynchronous | - Clock generated interrupt | - Regular interrupt with no fixed period | - Externally generated interrupt

## Slide 5: Concept: System utilization
The percentage of usage of a system / resource
  Indicates buffers available for handling excursions
Utilization (%) | Category | Application(s)
0-25 | Excess resources | -
26-50 | Very safe | High consequence system
51-68 | Safe | Critical system
69-70 | Theoretical limit | Average system
71-85 | Questionable | Overloaded system
86-100+ | Dangerous | Stressed system

## Slide 6: System design – Issues and dimensions
System specification
  Form factor
  Operating environment
  Temporal behavior
Selection of HW and SW components
  Hardware
    Cost, availability, manufacturability
  Software
    Programming language and development nuances
System testability
System interoperability (standards compliance)
System fault tolerance requirement
System reliability

## Slide 7: Concept: Real-time systems
Systems defined by constraint(s) on
  Event to System-response time
Systems that guarantee response
  Within specified time constraints (called ‘deadlines’)
Formal definition
  A real-time system is one which controls an environment by receiving data, processing it, and returning the results sufficiently quickly to affect the environment at that time
Usually used for mission-critical, high-consequence systems

## Slide 8: Concept: RTOS
A real-time operating system (RTOS) is an OS
  Intended to serve real-time applications on real-time systems
Prime characteristics:
  High level of consistency regarding time taken to complete a task
  Low ‘jitter’ – variability in response time
  Deadlines met deterministically by proper task scheduling
  Minimal interrupt and thread-switching latency
Hard vs Soft real-time
  Hard real-time: Late response is a ‘wrong’ response
  Soft real-time: Late response can be tolerated within limits

## Slide 9: Real-time systems: Misconceptions
Real-time systems are ‘fast’ systems
Real-time task scheduling is a solved problem
There are universal methodologies for real-time system specification and design
Using a well-known commercial real-time OS is enough to make real-time products

## Slide 10: Real-time world - a glimpse into issues

## Slide 11: RT issues: Strange problem
Assembly plant
  Temperatures change at different places
Monitoring system
  Equipped with 2 temperature sensors
    At different places in an assembly plant
    Sensors give interrupts when they have temperature data
  Monitors if the 2 temperatures are equal
  Raise an alarm if they are not!
System deployed, strange observation:
  As temperatures changed in the plant
  Even if the temperature at all places was equal
    System sometimes sounds the alarm
Why are we getting false alarms?

## Slide 12: RT issues: Strange problem code
int Temps[2]; //global shared data
void interrupt ReadTemps()
{
Temps[0] = ReadSensor(1); // value from Sensor #1
Temps[1] = ReadSensor(2); // value from Sensor #2
}
void main(void)
{
int temp0, temp1;
while (1)
{
temp0 = Temps[0];
temp1 = Temps[1];
if (temp0 != temp1)
SoundAlarm();
}
}
Interrupt code changes values while main code is using them
What if interrupt comes between these reads?

## Slide 13: RT issues: Shared data problem – try.1
int Temps[2]; //global shared data
void interrupt ReadTemps()
{
Temps[0] = ReadSensor(1); // value from Sensor #1
Temps[1] = ReadSensor(2); // value from Sensor #2
}
void main(void)
{
while (1)
{
if (Temps[0] != Temps[1])
SoundAlarm();
}
}

## Slide 14: RT issues: Shared data problem – try.2
int Temps[2]; //global shared data
void interrupt ReadTemps()
{
Temps[0] = ReadSensor(1); // value from Sensor #1
Temps[1] = ReadSensor(2); // value from Sensor #2
}
void main(void)
{
int temp0, temp1;
while (1)
{
DisableInterrupts();
temp0 = Temps[0];
temp1 = Temps[1];
EnableInterrupts();
if (temp0 != temp1)
SoundAlarm();
}
}
Disabling interrupts during the ‘critical section’ seems to solve the problem
But is this really a good solution?
Critical section

## Slide 15: Interrupt disabling - Issues
System becomes less responsive
  Time interval(s) for which interrupts are disabled
Critical interrupts may be lost!
  Specially high-consequence devices
Lessons for coding ISRs
  Write short, sweet ISRs
  Avoid spending too much time inside an ISR
  ISR should return to ‘normal code’ as soon as possible!

## Slide 16: RT issues: Shared data problem – try.3
int TempsA[2], TempsB[2];
bool UsingA = true; // boolean flag, can be either true or false
void interrupt ReadTemps()
{
if (UsingA == true)
{ TempsB[0] = ReadSensor(1); TempsB[1] = ReadSensor(2); }
else
{ TempsA[0] = ReadSensor(1); TempsA[1] = ReadSensor(2); }
}
void main(void)
{
int temp0, temp1;
while (1)
{
if (UsingA == true)
{ temp0 = TempsA[0]; temp1 = TempsA[1]; }
else
{ temp0 = TempsB[0]; temp1 = TempsB[1]; }
UsingA = !UsingA; // reverse the flag’s state
if (temp0 != temp1)
SoundAlarm();
}
}
Mutual exclusivity using a boolean flag

## Slide 17: embedded software architecture

## Slide 18: Embedded software architecture
Software architecture
  How to arrange code and get things done in a system/application
  Depends on:
    Prowess of the system, component topologies
    Nature and number of things to be done
    Time limits on getting these things done
Embedded domain software architectures:
  Round-robin
  Round-robin with interrupts
  Function queue scheduling
  RTOS

## Slide 19: Architecture: Round-robin – Code
// System with N devices
void main(void)
{
while(1)
{
if (Needs_service(Device1))
Service_Device1();
if (Needs_service(Device2))
Service_Device2();
…
if (Needs_service(DeviceN)
Service_DeviceN();
}
}
Poll each device, and serve if needed

## Slide 20: Architecture: Round-robin – Study
Pros
  Very simple to code
  Straightforward
  No interrupts
Cons
  If a device needs servicing faster than the ‘cycle time’
    It has to wait!
    Worst case: wait for (N-1) device servicing!
  If any single device servicing is lengthy
    All other devices suffer!
  No interrupts or concept of priority

## Slide 21: Architecture: RR w/interrupts – code
Interrupt code
// Per device flag to indicate if it needs service
bool Dev1 = false;
…
bool DevN = false;
void interrupt Set_Dev1_Flag()
{
Dev1 = true;
}
…
void interrupt Set_DevN_Flag()
{
DevN = true;
}
Main code
void main()
{
while(1)
{
if (Dev1==true) Service_Device1();
…
if (DevN == true)
Service_DeviceN();
}
}

## Slide 22: Architecture: RR w/interrupts – study
Code structure
  ISR code
    Only sets flags – hence, ensures fast ‘initial’ reactions to devices
  Main code, and service code (called ‘task code’)
    Do the actual work
Elementary concept of priority
  Dev1 > Dev2 > … > DevN (sort of!)
  But only for flag setting
    Task code is at same priority for all devices
Need to juggle polling order in main code
  Depending on device priorities

## Slide 23: Concept: Queue
FIFO (First In, First Out) structure of elements
  Of finite, pre-defined length
Has 2 ends: Front (head) and Back (tail)
  Elements enter at Back – called Enqueue operation
  Elements exit at Front – called Dequeue operation
  Elements exit in the same order that they entered

## Slide 24: Concept: Queue of function pointers
The nature of a Queue
  Depends on its elements
What if a Queue’s elements are ‘function pointers’?
  Enqueue operation
    Put a function pointer into the queue’s tail
  Dequeue operation
    Get a function pointer from the queue’s head

## Slide 25: Architecture: Function Queue Scheduling
FQS Concept:
  Schedule using Queue of Functions
    Queue elements are Function pointers
System with N devices
  N task codes, handled by N functions, with same API/signature
    void Service_Dev1(void);
    void Service_DevN(void);
  Define a function pointer
    typedef void (*serv_func_ptr)(void); // new type, same API
  Observe these statements
    serv_func_ptr = &Service_Dev1; // points to Dev1 code
    *serv_func_ptr(); // will run Dev1 code!
    serv_func_ptr = &Service_DevN; // points to DevN code
    *serv_func_ptr(); // will run DevN code!

## Slide 26: FQS: Queue operations
Enqueue
  Input is a function pointer
  Sends this function pointer to the queue’s tail
    void enqueue(serv_func_ptr in_function);
  Usage
    Put Service_Dev1()to the queue tail
      enqueue(&Service_Dev1);
Dequeue
  No input
  Output is a function pointer from the queue’s head
    serv_func_ptr dequeue(void);
  Usage
    Get the function out from the queue’s head
      out_function = serv_func_ptr dequeue();
    Call it by dereferencing the function pointer
      *out_function();

## Slide 27: FQS: Functioning
ISR code
  Enqueue that Device’s Service function
    To the queue’s tail
Main code
  Keep dequeue’ing from the queue’s head
    Obtain a function pointer
  Dereference this function pointer
    Run the corresponding service function

## Slide 28: FQS: Code snippets
Interrupt code
void interrupt Handle_Dev1()
{
enqueue(&Service_Dev1);
}
…
void interrupt Handle_DevN ()
{
enqueue(&Service_DevN);
}
Main code
void Service_Dev1()
{
// Service Dev1
}
void Service_DevN()
{
// Service DevN
}
void main()
{
serv_func_ptr a;
while(1)
{
a = dequeue();
*a();
}
}

## Slide 29: Architecture: FQS – study
Pros
  Effect of FQS functioning
    Service functions run in the same order they were qeueued up
    Devices can be serviced more than once – no cycle concept
      Dev1, Dev6, Dev4, Dev1, Dev1, … etc.
Cons
  Devices with tendency to interrupt often
    Are favoured with more service
  Device with big/long service function
    If queued and scheduled
      Can hog up time and hold up the system

## Slide 30: Architecture: RTOS
RTOS (Real-time operating system)
  Executes service code functions as individual tasks
    Tasks (could) have priority attributes
  Provides task creation, deletion facilities
  Runs a scheduler (usually part of kernel)
    Decides the time sequence of tasks to run
    Slices CPU time across multiple tasks
      Switches tasks from slice to slice
  Provides signaling services
    Send(), Wait()

## Slide 31: RTOS: Partitioning and Concepts
Code partitioned into:
  ISR code
  Service code (called Task code)
  Main code
ISR code
  Send a unique signal (per device)
Task code
  Wait for device-unique signal
  Run the device code
Main code
  Initialize system
  Start all tasks
Concepts
  Task
    A concurrent activity
    Has its own thread of control
      With its own stack, context, etc.
  Semaphore
    An inter-task communication mechanism for synchronization
    A mechanism to keep track of resource usage
  Mutex
    A locking mechanism to resolve
      Conflicting requests from different tasks
      For the same resource

## Slide 32: RTOS: Code snippets
Interrupt code
void interrupt Handle_Dev1()
{
Send_Signal1();
}
…
void interrupt Handle_DevN()
{
Send_SignalN();
}
Main and task code
void Task1()
{
Wait_for_Signal1();
Service_Device1();
}
void TaskN()
{
Wait_for_SignalN();
Service_DeviceN();
}
void main(void)
{
// Start Task1
…
// Start TaskN
}

## Slide 33: Architecture: Comparisons
 | Priorities | WCRT | Stability to code changes | Complexity
Round-robin | None | Sum of all task codes | Very poor | Very simple
Round-robin w/interrupts | ISR, all tasks at same priority | Sum of all task codes + ISR times | Poor, lot of tuning needed | Shared data problem, ISR writing
Function Queue Scheduling | ISR, tasks in priority order | Time of longest task code + ISR times | Queue management is critical | Shared data problem, Queue code
RTOS | ISR, tasks in priority order | 0 + ISR time | Very good | High (needs kernel)

## Slide 34: Thank you!