## Slide 1: rtos
Basics

## Slide 2: RTOS: Components
Kernel
  System resource manager
  Includes the Scheduler
    Schedules tasks for execution
Task
  Implements specific task code
  Has its own ‘state’ / ‘context’
    PC, Registers, Stack, etc.
ISRs
  Interrupt service routines
Layering starts!
  Tasks have to go through the RTOS
    To interact with HW!

## Slide 3: RTOS: Task structure
Task is composed of:
  Task code: Implementing function
  Task data: Variables local to the task
  Task ‘state’ / ‘context’: What the task is doing
Task Control Block (TCB)
  A data structure storing task properties
    When Task is not running
  Unique per task
  Typical TCB structure:

## Slide 4: RTOS: Task state / status
Executing
  Running on the CPU
Ready
  Could run, but can’t since another is running on the CPU
Blocked
  Cannot run, waiting for some resource to be available
Dormant
  Created, but not ready to run yet
Terminated
  No longer active
RTOS implements an FSM for each task
Manages task state transitions

## Slide 5: RTOS: Task state machine
Task activated
Task got resrc
Task got resrc
Task waiting
Task killed
Task killed
Task scheduled
Task just created
Dormant
Ready
Executing
Terminated
Blocked
Task yields
Task active

## Slide 6: RTOS: Scheduler
The RTOS Scheduler
  Implements the task state machine
  Maintains a list of tasks in 2 states
    Executing
    Ready
    Other states don’t matter much
      Blocked task has to unblock itself
      Dormant task has to be activated
      Terminated task is anyway dead
  Switches between tasks
    Context switch algorithm
      Save current task’s context into its TCB
      Find new task to run
      Restore context from its TCB
      Run new task

## Slide 7: RTOS: Task/context switching options
A task/context switch in an RTOS could be:
  Non-preemptive (Cooperative)
    Passive Scheduler
    A running / executing task keeps running till:
      It yields CPU time voluntarily
      It gets blocked on some unavailable resource
    Depends on the good behavior of all tasks
    Rarely used in today’s systems
  Preemptive
    Proactive Scheduler
    Scheduler switches tasks abruptly due to:
      A time slice expiry (for equal priority scenarios)
      A higher priority task / event (interrupt)

## Slide 8: RTOS: Preemptive scheduler functioning
System with 3 tasks
  Task1, Task2, Task3, and 1 interrupt (handled by ISR1)
  Priority wise:
      ISR1 > P(Task3) > P(Task2) > P(Task1)
Scheduler runs highest priority task
  Lower priority task is ‘suspended’
  Lower priority task ‘resumes’ run
    After higher priority task is done
ISR1 is at highest priority
  It suspends any and all tasks to run
Sample RTOS trace

## Slide 9: RTOS: Resource management
Embedded systems are (severely) resource limited
  Multiple tasks have to share resources
  Each resource sharing creates its own issues
    RTOS has its own way of mitigation
Resource | Issue | Mitigation
CPU time | Contention - All tasks want to run now! | Preemption, Time-slicing, Priority execution
Data (global) | Shared data problem | Mutual exclusion flags
Task code | Shared code problem | Function reentrancy
Hardware (pin, register, bus) | Contention and usage conflict | Mutexes, Semaphores

## Slide 10: RTOS: Shared code problem
Task 1 (use sensors 1,2)
Task 2 (use sensors 3,4)
// Sensor3=20 ⇒ Sensor4=20
void task (int sen1, int sen2)
{
tmp = read(sen1);
write(sen2) = tmp;
}
2 equal priority tasks – share code and data
int tmp; // shared global variable
// Sensor1=10 ⇒ Sensor2=10
void task (int sen1, int sen2)
{
tmp = read(sen1);
write(sen2) = tmp;
}
task() is called non-reentrant

## Slide 11: RTOS: Reentrancy
RTOS Scheduler keeps switching tasks
  Depending on various policies and conditions
    Time slice expiry
    Priority pre-emption
    Interrupt servicing
    One/more of the above!
Hence, all task (as well as other) functions
  Need to be reentrant
Reentrancy
  Multiple invocations can safely run concurrently
  System behavior does not change if a function is reentered
    Any number of times from any number of points
Reentrant functions
  Should not use globals
  Should not call any non-reentrant functions

## Slide 12: RTOS: Semaphore
Semaphore
  A variable or data-type used to control access
    To a common resource
    By multiple tasks / threads / processes
    In a concurrent system (like an OS/RTOS)
Types:
  Counting semaphore
    Supports arbitrary resource count
    Used for controlled access to a pool of resources
  Binary semaphore
    Supports binary access (available / unavailable)
    Used for controlled access to a single resource

## Slide 13: RTOS: Mutex
Mutex
  A locking mechanism used to control access
    To a single resource
    By multiple tasks / threads / processes
    In a concurrent system (like an OS/RTOS)
  Behaves very much like a binary semaphore
    Implements mutual exclusion concurrency
  Has concept of ownership
    Only the task / thread that locked it can unlock it
In both mutex and semaphore
  A task wanting to use an unavailable resource
    Has to wait – go to a ‘blocked’ state

## Slide 14: RTOS: Mutex vs Semaphore
Mutex
Semaphore

## Slide 15: RTOS: Scheduling policies
Some policies used for scheduling task execution
  Round-robin (RR)
    All tasks at same priority
    CPU time is sliced across different tasks
    Called ‘fair’ scheduling
  Fixed priority – Rate monotonic (RM)
    Priority preemptive kernel
    Set of periodic tasks
    Tasks with shorter periods are given higher priority
  Dynamic priority – Earliest deadline first (EDF)
    Priority preemptive kernel
    Ready task with earliest deadline has highest priority

## Slide 16: RTOS: Memory management
No! (DO-178B)
  All memory usage needs to be decided upfront
Dynamic memory allocation
  Through standard C functions: malloc() / calloc() / free()
    Severely restricted, if at all available
    Dynamic memory involves heap management
      Increases response ‘jitter’
RTOS memory management technique: Pools
  Divide available memory into equal-sized pools
  Run a restricted pool manager

## Slide 17: Priority inversion

## Slide 18: RTOS issue: Priority inversion – Case
Mars Sojourner Pathfinder (1996)
  Wind River System’s VxWorks RTOS based rover
    Worked well for a while on landing and deployment on Mars
      Later, suspicious hang-ups and reboots started
    Glitches had been observed during ground testing
      Engineers attributed it to faulty hardware
    Analysis revealed task restarts due to watchdog timer expiry
      Frequent resets hampered its ability to collect critical data
      Lifetime of the spacecraft was limited – leading to lost time-cycles
  The problem was identified to a software failure
    A high priority task on the system was blocked from running
    While a lower priority task ended up consuming CPU

## Slide 19: RTOS: Priority inversion – Root cause
Pathfinder System:
  Tasks: Task1, Task2, Task3
  1 shared resource, locked by mutex-lock S
  Priorities: P1> P2 > P3
  Task code template (CS indicates critical section):
    Task1: { … lock(S); CS1(); unlock(S); … }
    Task2: { … … … }
    Task3: { … lock(S); CS3(); unlock(S); … }
Priority inversion – P2 trumps P1

## Slide 20: RTOS: Priority inversion – solution.1
Priority Inheritance Protocol (PIP)
  Temporarily raise the priority of a low priority task
    But only if it is blocking a high priority task
  On leaving the CS, the priority reverts back to normal (low)
  Low priority task thus inherits the priority of the high priority task

## Slide 21: RTOS: Priority inversion – solution.2
Priority Ceiling Protocol (PCP)
  Priority ceiling [PC(S)]: Highest priority of all tasks that use S
  Rule: Task P trying to lock S will be suspended
    Unless pri(P) > PC(S) for all S currently locked by other tasks
  Example: 3 tasks (P1, P2, P3), 2 locks (S1, S2)
    Assume: S1 is used by P1 and P2, S2 is used by P2 and P3
      PC(S1) = max[pri(P1), pri(P2)] = pri(P1)
      PC(S2) = max[pri(P2), pri(P3)] = pri(P2)
P3 gets ceiling of S2

## Slide 22: RTOS: PCP vs PIP
PCP vs PIP
  Relationship
    PCP is considered to be a super-set of PIP
      Incorporates more checks and conditions
  Behavior
    PIP is bad at handling chain blocking and race conditions
      PCP handles chain blocking well
      PCP minimizes inheritance related inversions
    Blocking time is deterministic in PCP*
  Scalability
    PCP is considered more scalable compared to PIP
  Implementation
    PIP is easier to implement – less complex code
    PCP is much more complicated to implement and debug

## Slide 23: Thank you!