## Slide 1: Freertos
Introduction

## Slide 2: What is FreeRTOS?
A free, open-source real-time operating system (RTOS)
  Developed by Richard Barry (Director, Real Time Engineers Ltd., UK)
  15+ years old, currently at v10.4.0
  Dual licensing
    Free: FreeRTOS (MIT open source license)
    Commercial:
      OpenRTOS™ - Technical support
      SAFERTOS™ - Domain certified derivative
      FreeRTOS+ - Libraries for networks, file-systems, etc.
  Meant for microcontrollers and small microprocessors
Features
  Lucid, simple approach
    Basic kernel is just 3 C files
  Tiny, power-saving kernel
    Some architectures feature a tick-less power saving mode
  Supported on 40+ architectures
    ARM, PIC, AVR, Marvell, MIPS, NXP, RISC-V, …
    Full details: https://freertos.org/RTOS_ports.html
  www.freertos.org

## Slide 3: FreeRTOS: Functionalities
Designed from the ground up
  To fit onto very small embedded systems
Implements
  Simple API-based task management
    Preemptive tasks
    Support for priority
  Unlimited number of tasks and priorities
  Minimalistic memory handling (optional)
  Bare-minimum API for synchronization
    Queues, Semaphores, Mutexes
Tiny footprint
  4.3Kbytes on ARM7
Written in C
  Supports a variety of compilers (gcc, PIC C18 MPLAB, VC++, …)

## Slide 4: FreeRTOS: Tasks – Task functions
Unlimited number of tasks can run
  As long as hardware and memory can handle it
Support for cyclic (periodic) and acyclic tasks
API/signature for a task function:
  void task_function(void *pvParameters);
Inside a task function:
  void task_function(void *pvParameters)
  {
  int my_var; // local variable in task
  for (;;)
  {
  // Task code implementation
  }
  return; // Ideally, should not reach this point
  }

## Slide 5: FreeRTOS: Task handling API - Create
portBASE_TYPE xTaskCreate(
TaskFunction_t pvTaskCode,
  const char * const pcName,
  configSTACK_DEPTH_TYPE usStackDepth,
  void *pvParameters,
  UBaseType_t uxPriority,
  TaskHandle_t *pxCreatedTask
  );
Argument | Remarks
pvTaskCode | Pointer to the task function
pcName | Human-readable string naming the task
usStackDepth | Depth of the task stack
pvParameters | Optional parameters sent to the task
uxPriority | Priority of the task
pxCreatedTask | Pointer to the created task (handle)

## Slide 6: FreeRTOS: Task handling APIs
Delete a task
  void vTaskDelete( TaskHandle_t xTask );
Get task priority
  UBaseType_t uxTaskPriorityGet( TaskHandle_t xTask );
Set task priority
  void vTaskPrioritySet( TaskHandle_t xTask, UBaseType_t uxNewPriority );
Suspend a task
  void vTaskSupend( TaskHandle_t xTask );
Resume a suspended task
  void vTaskResume( TaskHandle_t xTask );
Get a delay
  void vTaskDelay( const TickType_t xTicksToDelay);
Get list of tasks in the system
  void vTaskList( char *pcWriteBuffer );

## Slide 7: FreeRTOS: Scheduler internals
Concept of ‘tick’
  Smallest time-slice the Scheduler is aware of
On every tick, Kernel gets a ‘tick’ interrupt
  Scheduler
    Decides which task to switch to
      Consults Ready and Waiting task lists
      Looks at task priorities
    This is done in the Tick interrupt ISR
      Needs to be extremely fast

## Slide 8: FreeRTOS: Scheduler in action
Scheduler
  Juggles between switching various tasks
    Different priorities, rates (periods), events, etc.
  Runs an ‘idle’ task
    When nothing else needs to run

## Slide 9: FreeRTOS: Code structure
ISRs, Task code
void interrupt HandleInterupt ()
{
// ISR code
}
void Task1(void *Task1_Params)
{
while(1)
{
// Task1 code
}
}
void TaskN(void *TaskN_Params)
{
while (1)
{
// TaskN code
}
}
Main code
void main(void)
{
System_Init();
// Task1
xTaskCreate(…);
…
// Task N
xTaskCreate(…);
vTaskStartScheduler();
return;
}

## Slide 10: Advantages of using a real-time kernel
A real-time kernel (like FreeRTOS):
  Abstracts away timing information and consideration
  Eases maintainability and extensibility of modules
  Increases code modularity
  Enhances collaborative (team) development
  Enables better code re-use
  Improves system and resource usage efficiency
  Enables tracing and background checks (as part of idle time)
  Betters power management (derived from efficiency boost)
  Makes interrupt handling flexible
  Addresses mixed processing requirements

## Slide 11: FreeRTOS summary
What is FreeRTOS?
  Licensing options
Applicability to embedded system product development
Elementary look at
  Task handling APIs
  Kernel (scheduler) internals
Material is based on:
  Nicolas Melot’s “Study of an Operating System: FreeRTOS”
  Link:
    http://wiki.csie.ncku.edu.tw/embedded/FreeRTOS_Melot.pdf

## Slide 12: Thank you!