## Slide 1: PIC18F Serial Interfaces
RS232
I2C
SPI

## Slide 2: Serial Port (RS232) basics
Serial vs Parallel – pros and cons
Serial port data transfer types
  Simplex, half-duplex, full-duplex
  Synchronous and asynchronous transmission
Asynchronous
  Start (low) and Stop (high) bits, Parity bits
  Data transfer rate vs Baud rate
Most common: 9600/8-N-1
  9600 baud, 8-data-bits, No-parity-bits, 1 stop-bit

## Slide 3: Serial Port (RS232) physical layer
RS232 is a “Point-to-Point” communication bus
Handshaking pins (h/w flow control)
  DTR (data transmit ready), DSR (data set ready)
  RTS (request to send), CTS (clear to send)
Data transfer pins
  Tx for transmission
  Rx for reception
  Gnd
Voltage levels
  RS232
    Logic 1 => -3v to -25V
    Logic 0 => +3V to +25V
    -3V to +3V is undefined
  TTL
    Logic 1 => 2V to VCC
    Logic 0 => 0V to 0.8V
RS232 and TTL are not compatible!

## Slide 4: PIC18 Serial Port Registers
Tx and Rx pins are shared with PORTC (Tx/RC6, Rx/RC7)
TTL compatible, not compatible with RS232
  So a line driver MAX232/233 is used for RS232 interface
Interrupts to indicate data transfer is complete
  TXIF, RXIF flags (part of PIR1) – interrupt indicators
  TXIE, RCIE flags (part of PIE1) – interrupt enablers
Register | Purpose | Remarks
SPBRG | Baud rate decider | Baud = Fosc / [64(X+1)]
TXREG | Transmit register | 
RCREG | Receive register | 
TXSTA | Transmit status/control | 
RCSTA | Receive status/control | 

## Slide 5: PIC18 Serial Port: TXSTA
TXSTA
  CSRC: clock select (not used in async mode)
  TX9: Enable 9-bit data transmit
  TXEN: Transmit enable
  SYNC: Async / sync mode
  BRGH: High baud rate select
  TRMT: Transmit shift register status
  TXD9: 9th bit of transmit data
TXSTA value for normal data transfer
  B’0010 0000’ or 0x20
CSRC
TX9
TXEN
SYNC
0
BRGH
TRMT
TX9D

## Slide 6: PIC18 Serial Port: RCSTA
RCSTA
  SPEN: Serial port enable
  RX9: Enable 9-bit data receive
  SREN: Single receive enable (not used in async)
  CREN: Continuous receive enable
  ADDEN: Address detect enable
  FERR: Framing error bit
  OERR: Overrun error bit
  RX9D: 9th bit of receive data
RCSTA value for normal data transfer
  Enable SPEN (serial port enable)
SPEN
RX9
SREN
CREN
ADDEN
FERR
OERR
RX9D

## Slide 7: PIC18: Serial data transmit
Load TXSTA (0x20)
Load SPBRG
Make RC6/TX output
Enable SPEN of RCSTA
Check if previous transfer is complete by polling TXIF of PIR1
Move data to TXREG
MOVLW 0x20
MOVWF TXSTA
MOVLW 0x81
MOVWF SPBRG
BCF TRISC, TX
BSF RCSTA, SPEN
DONE MOVLW a’B’
L1 BTFSS PIR1, TXIF
BRA L1
MOVWF TXREG
BRA DONE

## Slide 8: PIC18: Serial data receive
Load RCSTA (0x90)
  SPEN, Continuous receive
Load SPBRG
Make RC7/RX input
Check if entire byte has come in by polling RCIF of PIR1
Move data from RCREG to W
MOVLW 0x90
MOVWF RCSTA
MOVLW 0x0F
MOVWF SPBRG
BSF TRISC, RX
L1 BTFSS PIR1, RCIF
BRA L1
MOVF RCREG, W
BRA L1

## Slide 9: PIC18: Higher baud rates
By taking BRGH bit of TXSTA to 1, we can quadruple the baud rate
  Examples:
    BRGH=0, SPBRG=15 gives us a baud rate of 9600
    BRGH=1, SPBRG=15 gives us a baud rate of 38,400
    BRGH=0, SPBRG=4 gives us a baud rate of 28,800
    BRGH=1, SPBRG=4 gives us a baud rate of 115200

## Slide 10: I2C: Introduction
I2C is a multi-master, serial, single-ended communication bus
Invented by Philips / NXP
Very popular bus for connecting/interfacing peripheral devices to micro-controllers / micro-processors
  Reading config data from DDR1 SDRAM, DDR2 SDRAM (DIMM)
  Controlling low speed ADC’s and DAC’s
  Controlling OLED’s in smartphones
  Accessing NVRAM chips/modules on SoC’s
  Controlling monitor color, contrast, hue (Data Display Channel DDC)
  Controlling RTC’s
  Reading hardware monitors, temperature sensors
Royalty-free since Oct 2006
  Though valid I2C address from NXP has costs
Bus speeds
  Standard I2C: 100kHz
  Fast: 400kHz
  Hi-speed: 3.4MHz
  Fast mode plus: 1MHz
  Ultra fast mode: 5MHz

## Slide 11: I2C: Physical layer
2 lines / pins
  SCL (clock)
  SDA (data)
Standard TTL voltages
  3.3V / 5V
An open-drain / open-collector bus
  Needs pull-up resistors to hold SDA/SCL at Logic 1
  Wired OR logic – any device can pull the line LOW
Multi-master bus with 8 (actually 7)/10-bit addresses
  Multiple masters (usually microcontroller / microprocessor)
  Multiple slaves
Roles:
  Master initiates communication, drives the clock (SCL), performs bus arbitration
  Slave responds to master, gives/takes data on SDA

## Slide 12: I2C: Signalling
I2C device modes of operation
  Master send – slave receive <data/address>
  Master receive – slave send <data>
Communication start: Master sends “START”
Communication end: Master sends “STOP”
START
  SCL stays HIGH, SDA goes from HIGH to LOW
STOP
  SCL stays HIGH, SDA goes from LOW to HIGH

## Slide 13: I2C: SCL, SDA relationship
Pin-wise:
  SCL pin is clock; driven by master
  SDA pin is data; driven by master / slave
SDA stable when SCL is HIGH
  This is when the data is “sampled” on the line by master/slave
SDA line is written MSB-first:
  8-bits, could be:
    7-bit address + R/W
    8-bit data
  9th bit is driven LOW by slave as an ACK

## Slide 14: I2C: WRITE (Steps)
Data transfer steps for WRITE:
  Slave identification by device address (W)
    Master sends START code
    Master sends 7-bit slave address (MSB first)
    Master sends R/W-bit (0 means write)
    Slave sends 1-bit (with value 0) as ACK
  Slave register address send-out
    Master sends 8-bit address in the slave, that it wishes to write into
    Slave sends 1-bit (with value 0) as ACK
  Slave data send-out
    Master sends 8-bit data to Slave
    Slave sends 1-bit (with value 0) as ACK
  End of transfer
    Master sends STOP code

## Slide 15: I2C: WRITE (Bus timing)

## Slide 16: I2C: READ (steps)
Data transfer steps for READ:
  Slave identification by device address (W)
    Master sends START code
    Master sends 7-bit slave address (MSB first)
    Master sends 1-bit (0 means write)
    Slave sends 1-bit (with value 0) as ACK
  Slave register address send-out
    Master sends 8-bit address in the Slave it wishes to write into
    Slave sends 1-bit (with value 0) as ACK
  Slave identification by device address (R)
    Master sends START code
    Master sends 7-bit slave address (MSB first)
    Master sends R/W-bit (1 means read)
    Slave sends 1-bit (with value 0) as ACK
  Slave data send-out
    Slave sends out 8-bit data
    Master sends 1-bit (with value 1) as NACK
  End of transfer
    Master sends a STOP code

## Slide 17: I2C: READ (Bus timing)

## Slide 18: I2C: Clock stretching
If a slave device cannot cope up with the speed of data transfers / demand from the master, it can pull the SCL line low and “ask the master to hold”
  This is called clock stretching
The master should keep a tab on the SCL line
  Initiate the next data transfer only when SCL is high

## Slide 19: I2C: Bus arbitration
All masters should monitor the SDA line for START and STOP codes
  Transmit only when the bus is free
But sometimes, 2 masters may start transmitting at the same time
  Here, I2C uses the SDA line for bus arbitration
  SDA is open-drain
    A master pulling SDA LOW will win over a master keeping SDA HIGH
  A master keeps a tab on SDA and compares it with the level it expects
    If a master sent a ‘0’ and got SDA LOW
      Everything is alright
    If a master sent a ‘1’ and got SDA HIGH
      Everything is alright
    If a master sent a ‘1’ and got SDA LOW
      Some other master is driving the bus
    This master then “loses” bus arbitration
    It will retransmit after the current transaction finishes

## Slide 20: I2C on PIC18F
PIC18F uses its MSSP for I2C and SPI
  Master synchronous serial port
MSSP registers
  SSPSTAT
  SSPCON1
  SSPCON2
  SSPADD
  SSPBUF

## Slide 21: SSPSTAT – Status Register
BF: Buffer Full
  In transmit mode, it gets set when data is written to SSPBUF and cleared when transmit is complete
  In receive mode, it gets set when data/address is received in the SSPBUF
UA: Update Address (10-bit address mode)
R/W: In master mode, 1 means TXMIT in progress
S: 1 means START sequence detected last, cleared during reset
P: 1 means STOP sequence detected last, cleared during reset
D/A: Data/Address indicator (in Slave mode)
CKE: Clock Edge Select bit (1=> Transmit on Active->Idle Clock)
SMP: 1 means disable slew rate control (slew rate disabled for low speeds like 100 Khz)
D/A
P
S
R/W
UA
BF
CKE
SMP

## Slide 22: SSPCON1 – Control Register 1
SSPM0-SSPM3: Mode select bits
  1111: I2C slave; 10-bit address, S-P interrupts enabled
  1110: I2C slave, 7-bit address, S-P interrupts enabled
  1011: I2C firmware controlled master, slave idle (bit bang)
  1000: I2C master, clock = Fosc / (4*SSPADD+1)
  0111: I2C slave, 10-bit address
  0110: I2C slave, 7-bit address
CKP: SCL clock release bit (1 => release), used in Slave mode
SSPEN: SSP enable bit (1 => enable)
SSPOV: Receive overflow indicator, SSPBUF overflow
WCOL: Write collision detection bit (1 => collision)
SSPEN
CKP
SSPM3
SSPM2
SSPM1
SSPM0
SSPOV
WCOL

## Slide 23: SSPCON2 – Control Register 2
SEN:
  Master: Start condition enable
  Slave: Stretch enable
RSEN: Repeated Start condition enable (master only)*
PEN: Stop condition enable (master only)*
RCEN: Receive enable bit (master only)
ACKEN: Ack sequence enable (master only)*
ACKDT: Ack data bit (master receive only)
ACKSTAT: Ack status bit [1 => NACK](master transmit only)
GCEN: General call enable
* Automatically cleared by hardware
ACKDT
ACKEN
RCEN
PEN
RSEN
SEN
ACKSTAT
GCEN

## Slide 24: SSPADD, SSPBUF, SSPIF
SSPADD determines the speed
Bus speed = Fosc / (4*SSPADD+1)
SSPBUF is an 8-bit register used for address/ data transfer
  Similar to TXREG and RCREG for serial port
SSPIF is the interrupt flag
  Set on getting an SSP interrupt
  Part of PIR1

## Slide 25: I2C on PIC board: Init Sequence
BSF SSPSTAT, 7 ;sampling done at the end of data output time
BCF SSPSTAT, 6 ;slew rate control disabled for standard speed
MOVLW D'49'
MOVWF SSPADD ;baud rate value for 100kHz
BSF SSPCON1,SSPEN ;enables serial port
BSF SSPCON1,SSPM3 ;
BCF SSPCON1,SSPM2 ;
BCF SSPCON1,SSPM1 ;
BCF SSPCON1,SSPM0 ;i2c Master mode, clock=Fosc/(4*(SSPADD+1))
;clock = 100kHz, Fosc = 20Mhz

## Slide 26: I2C on PIC: Start, Stop, Verify
I2CSTART
BSF SSPCON2,SEN ;START Condition Enable Bit
BTFSS PIR1,SSPIF ;wait for START enable(check SSP interrupt flag)
GOTO $-1 ;skip if set
BCF PIR1,SSPIF ;clear flag bit
RETURN ;return from subroutine
I2CSTOP
BSF SSPCON2,PEN ;STOP Condition Enable Bit
BTFSS PIR1,SSPIF ;wait for STOP condition(check SSP interrupt flag)
GOTO $-1 ;skip if set
BCF PIR1,SSPIF ;clear flag bit
RETURN ;return from subroutine
VERIFY
MOVWF SSPBUF ;loading data to SSPBUF for i2c write
BTFSS PIR1,SSPIF ;wait for data write(check SSP interrupt flag)
GOTO $-1 ;skip if set
BCF PIR1,SSPIF ;clear flag bit
MOVF SSPBUF,W ;loading working register with SSPBUF data
RETURN ;return from subroutine

## Slide 27: I2C on PIC: Write
Assumes data to be written is loaded into W register
I2C_WRITE
MOVWF tmp
CALL I2CSTART ;call for i2c START
MOVLW <address> ;writing Device Address with write enable
CALL VERIFY ;call for write verification
MOVLW <register address> ;writing Location Address
CALL VERIFY ;call for write verification
MOVF tmp, W ;Data to be written(ASCII)to device CALL VERIFY ;call for write verification
CALL I2CSTOP ;call for i2c STOP
CALL DELAY
CALL DELAY
RETURN

## Slide 28: I2C on PIC: Read
I2C_READ CALL I2CSTART ;call for i2c START
MOVLW <Address> ;writing Device Address with write enable
CALL VERIFY ;call for write verification
MOVLW <Register > ;writing Location Address
CALL VERIFY ;call for write verification
CALL I2CSTOP ;call for i2c STOP
CALL I2CSTART ;call for i2c START
MOVLW <Address with read> ;writing Device Address with read enable
CALL VERIFY ;call for write verification
BSF SSPCON2,RCEN ;synchronous reception enabled
BTFSS PIR1,SSPIF ;wait for data to be read(check SSP interrupt flag)
GOTO $-1 ;skip if set
BCF PIR1,SSPIF ;clear flag bit
BSF SSPCON2,ACKEN ;Master acknowledge enable
BSF SSPCON2,ACKDT ;send active low as acknowledgement from PIC to EEPROM
MOVF SSPBUF, W ;move the received data to working register
CALL I2CSTOP ;call for i2c STOP
RETURN

## Slide 29: I2C on PIC board: Projects
Write to I2C EEPROM and then read it back
User input (involves serial port):
  Accept input from serial port, write the string to I2C EEPROM
  Read it back in a separate program, display it on serial port

## Slide 30: SPI: Introduction
Serial Peripheral Interface (SPI)
  A 4-wire serial communication synchronous bus
  Operates in full-duplex mode
Popular bus for connecting/interfacing peripheral devices to microcontrollers / microprocessors
  Sensors (temperature, pressure), touchscreens, game controllers
  ADC’s, DAC’s
  Digital potentiometers, audio codecs
  Memory: Flash, EEPROM
  RTC’s, LCD’s, MMC/SD card variants
Devices communicate in Master/Slave mode
  No addressing concept on the bus
    Single master, multiple slaves
  Master initiates data frame
  Slave is selected (activated) for a transaction by an active LOW Slave Select (SS) line

## Slide 31: SPI: Bus topology
4-wire / 4-line bus
  SCLK (clock) [driven by Master]
  MOSI [Master Out Slave In]
  MISO [Master In Slave Out]
  SS (Active LOW) [Slave Select]
Number of SS lines increase with number of slave devices on the system

## Slide 32: SPI: Data transfer
Master selects the slave device by asserting the SS line in LOW mode
  If the slave device is slow, master waits for x cycles
Master then activates the clock on SCLK line
  Typically, clock frequency is few MHz
During each SPI clock cycle, a full-duplex data transmission occurs
  Master sends out a bit on MOSI, slaves reads it
  Slave sends out a bit on MISO line, master reads it
Transmission usually occurs with 8-bit registers on Master and Slave, connected in a “ring” format
Not all the bit transfers may be meaningful, they happen nevertheless

## Slide 33: SPI: Pros and Cons
Pros
  Full-duplex communication, higher throughput
  Protocol flexibility (arbitrary choice of word length)
  Simple hardware interfacing
    Low power consumption, no pull-up resistors
    No arbitration messiness
    No addressing schemes
    Slave uses master’s clock, no precision oscillators needed
  Clock speed can be arbitrary allowing high speeds
Cons
  4-wire interface means high real estate demand on embedded boards
  Supports only a single master
  No support for flow control by the slave (master slows down if it knows slave is slow)
  No support for ACK (receive acknowledgement) from either master / slave
  No error checking supported by default
  Difficult to add more slave devices (needs addition of an SS line on master and rewiring)
  Handles only short distances (compared to UART / RS232)